## Slide 1
Best Practices for Real-Time GNSS Network Administration Webinar July 31, 2013 2-5pm ET RTK/RTN Precision vs. Accuracy & Occupation Time Mark L. Armstrong, PLS – Geodesist Oregon State Geodetic Advisor NOAA’s, National Geodetic Survey mark.l.armstrong@noaa.gov
Notes: <number>

## Slide 2: First Things First
Look up the RTK rover receiver specifications
  What accuracy is the receiver (sensor) capable of?
  What will it take to get the most accuracy from the receiver?
Part of the benefits of using an RTN over single base RTK –
Limited/Reduced ppm error
UNDERSTAND THE ROVER SPECIFICATIONS
(RMS)
Notes: But before beginning the discussion about precision and accuracy for an RTK/RTN survey, we must know what accuracy the rover receiver is capable of? The manufacturer constructs a GNSS receiver, and attached an antenna to it. Then tested it to make sure it meets an accepted performance specification . It’s probably a good idea to know what those performance specifications are so that they may compared with real world field results?
One of the big benefits of using an RTN (corrector) over single base-rover RTK is that the first order ppm (part per million) error is eliminated (or drastically reduced) because ionosphere, troposphere and orbital errors are interpolated to the location of the rover. This enables centimeter level positioning at extended ranges over 10 km from a reference station.
Shown in the slide is a vendor rover positioning accuracy specification for a current model un-named GNSS receiver. The top one shown for RTK (L1+L2) gives the horizontal accuracy to be 10 mm (or 1 cm) RMS. So if you would like to compare results at 95% confidence (2 sigma) then double it. The vertical positioning accuracy in also shown below the horizontal.
Different manufactures may report accuracy specifications differently and sometimes have foot notes at the bottom of the spec sheet that provide more insight into how they determined the receiver accuracy.
<number>

## Slide 3: Precision vs. Accuracy measurement from RTN correctors
More questions?
Is there systematic bias, multipath, and atmospheric errors to overcome? Always some!
How is the accepted true (accurate) position determined?
Accurate - Accepted truth
Courtesy www.calguns.net
Notes: Here are the basic targets with bulls eye representing the conceptual difference between precision and accuracy.
The upper left target depicts ‘neither precision or accuracy’. The group of shots is loosely scattered and offset from the center of the bulls eye.
The upper right target depicts ‘precision but not accuracy’. The group of shots is tight but offset from the center of the bulls eye.
The bottom left target depicts ‘accuracy but not precision’. The group of shots is loosely scattered but appear uniformly around the bulls eye.
The bottom right target depicts ‘accuracy and precision’. The group of shots is tight and at the center of the bulls eye.
The center of the bulls eye reflects accuracy and thus the accepted true coordinate position. Since there is always some systematic bias, multipath, and atmospheric errors present with GNSS observations, the perfect condition of achieving both accuracy and precision will vary with different locations, time of day, and length of the observation time. As GNSS users, we know that additional RTK observation time on a mark provides more data, reflecting an improved mean precise coordinate.
<number>

## Slide 4: GNSS Errors and bias while observing a mark - to some degree always present and ever changing
Curtosy www.advanced-web-metrics.com
Notes: Here is another set of similar targets, but with a little more insight into the affect of GNSS errors and bias which to some degree is always present and ever changing.
Target 1 depicts an unbiased situation with an even loose scatter of points around the bull eye, but still not a tight precise group and not accurate although the mean of all the points may be fairly accurate.
Target 2 depicts a definite bias of points loosely scattered off to one side. Again not precise and not accurate and the mean of all of the points may only slightly improve the accuracy.
Target 3 also depicts a bias, as all of the points are off to one side but grouped tightly together showing precision but certainly not accuracy and meaning them does little to improve the accuracy.
Target 4 depicts the best of all possible conditions where there is no apparent bias and the points are grouped tightly together and centered on the bulls eye.
So RTN rover users may expect to see any and perhaps all of these conditions depending on the location of the mark being measured, the local GNSS errors present (atmospheric and multipath) combined with the receiver systematic error, the setup error, and the RTN network corrections applied.
<number>

## Slide 5: RTN Precision Measurement Field Testing
‘PRECISION’ is a computed statistical quantity to the source of the measurement – It is a measure of the uniformity or reproducibility of the result.
A rover measurement from the RTN shows precision of the observation and is normally recorded in the data collector as the average position of many 1 second measurements on a mark.
[This is not to be confused with the individual precision shown on the data collector screen for each 1 second shot.]
RTK point occupation time is the number of 1 sec. epochs logged over a given period of time to produce an average coordinate for a mark.
Notes: So precision by definition is a computed statistical quantity to the source of the measurement – It is a measure of the uniformity or reproducibility of the result.
A rover measurement from the RTN shows precision of the observation and is normally recorded in the data collector as the average coordinate of many accumulated 1 second measurements on a mark. [ This is not to be confused with the individual precision shown on the data collector screen for each 1 second shot logged of the total occupation time on the mark. ]
As an RTN rover operator, we do have control over how long we occupy a mark. We know that the more time we log (in 1 second epochs), while the satellites move across the sky in their orbits, the better the average coordinate of those logged 1 second epochs will be.
This you can test yourself by logging 1 second data for varying amounts of time and plotting the results. Then we could ask the question: how much occupation time is needed for a particular class of mark (say a kinematic project control point) given normal conditions of 6+ SV and normal to low GDOP?
If you were to look at the GNSS RTK Survey specifications for DOT’s across the country you would see a wide range of answers to that question.
<number>

## Slide 6: RTN Measurement Precision
Typical (normal) RTN precisions at the 95% confidence level:
  horizontal 2-3 cm
  vertical (ellipsoid height) 3-5 cm
  orthometric heights 5-7 cm (typical-using the NGS hybrid geoid model)
Exceptional RTN derived precisions at the 95% confidence level at the limit of RT technology:
  horizontal: ≤ 1 cm
  vertical (ellipsoid height) ≤ 1 cm
  orthometric heights ≤ 2 cm
http://www.geodesy.noaa.gov/PUBS_LIB/NGS.RTN.Public.v2.0.pdf
Notes: So generally speaking, what precisions are RTN’s capable of?
Typical measurement precision (will call normal) where RTN precisions at the 95% confidence level have horizontal results known to within 2-3 cm; vertical (ellipsoid height) results are within 3-5 cm; and orthometric height results within 5-7 cm (are typical-using the NGS hybrid geoid model).
Beyond that…
Exceptional measurement precision (requiring great attention to GNSS conditions and system procedures) is possible where RTN derived precisions at the 95% confidence level are at the current limit of real time technology with horizontal results within less than or equal to (≤) 1 cm; vertical (ellipsoid height) results also less than or equal to (≤) 1 cm, and possible orthometric heights less than or equal to (≤) 2 cm depending on the hybrid geoid model local accuracy.
The link at the bottom is to the “NGS Guidelines for Real Time Networks” which is the reference for much of what is in these slides.
<number>

## Slide 7: RTN Precision Measurement Field Testing
‘PRECISION’ is a computed statistical quantity to the source of the measurement. More measurements averaged = improved precision of the final coordinate.
RTN testing on a MARK:
-10 occupations at each interval in rotation for similar #SV and GDOP.
480s horiz. RMSE = 0.003 m
480s vert. RMSE = 0.009 m
Notes: Here’s a look at an example field precision test and I will add the accuracy part to it later in another slide, but for now were dealing with just precision. So as previously stated… Precision is the computed statistical quantity to the source of measurement. The more RTK measurements averaged over time will lead to an improved precision for the final coordinate.
Here is a graph of 50 RTK coordinates (shots) taken on a mark. 10 of the shots were for 480 seconds each or 8 minutes, 10 shots for 300 seconds each or 5 minutes, 10 shots of 180 seconds each or 3 minutes, 10 shots for 60 seconds each or 1 minute and 10 shots for 10 seconds each. Each shot within the group of 10 were rotated as time progressed so that they all had a similar range of satellite availability and GDOP. It took about 3 hours to do a full set. This is just one typical example of several taken. The legend and color codes are just to the right of the graph.
The circle shown in the graph represents a MAG nail which has a 13 mm diameter circle and is superimposed in the graph for a relational scale reference only, and it is centered on the average coordinate of all 10 of the 480 second shots (the longest ones). What we are looking for here is how observation time might affect the tightness of the groups.
Then as shown in the table to the right in red, 480 seconds (8 minutes), 9 out of 10 coordinates (of the dark green dots) landed on the head of the MAG nail. The light green dots show 10 occupations of 300 seconds each and 7 out of 10 landed in the MAG nail circle. For the yellow dots (representing 180 seconds) 5 out of 10 landed in the MAG nail circle.
For the 10 shots of 60 seconds each (orange dots) only 2 landed in the circle and last for the 10 shots of 10 seconds each (brown dots) only one landed in the MAG nail circle. This is just one example to show how… less occupation time per shot progressively enlarged and loosened the spread… which you might expect. This proved to be consistent over many independent tests taken at different locations within the RTN. Also tested was the distance from the RTN master station which varied from 1k to 26k with no apparent change in these results.
At the bottom of the slide, the root mean square error (RMSE) for the group of 10 shots of 480 second each was 3 mm for the horizontal coordinate and 9mm for the vertical. Just to give you an idea of the statistics related to that.
<number>

## Slide 8: What is Accuracy (Truth)
‘ACCURACY’ is a computed statistical quantity to the realization of the datum - Alignment of the RTN to the NSRS shows accuracy (typically by some method of post processing static observations of the RTN stations constrained by CORS coordinates)
http://www.geodesy.noaa.gov/PUBS_LIB/NGS.RTN.Public.v2.0.pdf
Accuracy is a measure of how the positions are aligned to “truth”
NGS wishes to encourage all RTN’s to provide users with alignment to the NSRS as the representation of truth.
  NAD 83 (horizontal and ellipsoid height)
  NAVD 88 (orthometric height)
Initial NGS guidelines support this alignment to the NSRS as: within 2 cm latitude and longitude, and within 4 cm ellipsoid height (95% confidence) using the CORS network weighted as truth.
Notes: So far I talked about precision and grouping of shots relative to occupation time.
Now the discussion turns to ‘ACCURACY’ which is a computed statistical quantity to the realization of the datum - Alignment of the RTN to the National Spatial Reference System shows accuracy (typically by some method of post processing static observations of the RTN stations constrained by CORS coordinates). This could be achieved through the use of OPUS or OPUS-Projects or other post processing software etc.
Accuracy is a measure of how the positions are aligned to “truth”. Of course the NGS wishes to encourage all RTN’s to provide users with alignment to the NSRS as the representation of truth. Therefore, accuracy would be relative to the alignment to our national datum's consisting of the current realization of NAD 83 (horizontal and ellipsoid height) and NAVD 88 (orthometric height).
Initial NGS guidelines desire RTN alignment to the NSRS as: to within 2 cm in latitude and longitude, and within 4 cm in ellipsoid height (@95% confidence) using the CORS network weighted as truth.
Again, here is the link at the bottom of the slide to the “NGS Real Time Network Guidelines” where there is more information on alignment to the NSRS.
<number>

## Slide 9: Field Test RTN Correctors Horiz. Precision vs. Accuracy
Meets the project survey specification - horizontal component 2cm @ 95% conf. accuracy guidelines.
Meets the receiver specification @ 95% conf.
Different datasets may yield different results.
Some Conclusions
Notes: Here is the slide shown previously that had just precision shown. Now… I’ve added accuracy and some comparisons to the bull eye targets shown in the earlier slides become obvious.
To determine what is accuracy for this remote field mark, an independent 4 hour static occupation was logged and then published to OPUS which returned a solution datasheet for the mark with peak-peak errors which are shown in the blue box around the coordinate labeled as the center of accuracy. The OPUS solution in this case represents the National Spatial Reference System as a TRUTH check.
Now we can see in this case there was some bias of the group of points shifted off to one side from the center of accuracy (the OPUS NSRS coordinate). But… the difference from the precision (8 minute average) center and the accurate (truth) center determined from OPUS was just about 1 cm and falling within our 2cm project specification goal.
And…also as seen within the 2 cm pinkish circle (centered on the average of all of the 480 epoch (8 minute) shots) are the longer RTK occupation times of 180 epochs (3 min) to 480 epochs (8 min) which appeared to met the receivers performance accuracy specification @ 95% confidence. Some of the shorter 60 second and 10 second epoch scattered shots fell outside of the circle appearing to not meet the receiver spec.
So you can field test RTN correctors (using a rover on a mark) to see if both precision and accuracy are within your project EXPECTED tolerance.
You may wish to test on multiple marks across the RTN to see how multipath, GDOP, and number of visible satellites might affect the result. Obtain average coordinates for varying times on a mark. Try observing for 8’ or perhaps even longer, down to 10” to see how the precision grouping changes with the different occupation times and then compare with a coordinate considered truth.
<number>

## Slide 10: Field Test Vert. Precision vs. Accuracy
The black horizontal line represents the 4 hour independent published OPUS solution and considered the truth (and representing the NSRS) in this case, while the blue horizontal straight line is the average of the 10 individual 8 minute RTK shots. They are about 1.6 cm apart vertically but many of the individual shots were outside the 4 cm vertical project specification.
Notes: Shown in this slide are all 50 of the same shots graphed by ellipsoid height. The black horizontal line represents the 4 hour independent published OPUS solution and considered the truth (and representing the NSRS) in this case, while the blue horizontal straight line is the average of the 10 individual 8 minute RTK shots.
They are about 1.6 cm apart vertically but many of the individual shots were outside the 4 cm vertical project goal. In this example case… the difference could be part GNSS error, part setup error, part receiver systematic error as the OPUS observation was observed in a different month and with different equipment.
<number>

## Slide 11
Survey Project Standards
How good is good enough?
Review typical accuracy spec. Only way to know and understand the working accuracy is to test.
Notes: If RTN rover users have a project survey guideline or standard for accuracy to follow, how will they know if they are actually getting the results they are trying to achieve?
This table comes from the NGS “User Guidelines for Single Base Real Time GNSS Positioning” and shows 4 different accuracy classes depending on the mark application with varying redundancy and observation time etc.
The only way to really know and understand the working precision and accuracy is to test across the network to see if following such a Accuracy Class meets the goal? RTN Administrators and users may want to develop their own guidelines for rover survey operation based on real precision and accuracy field testing across the RTN coverage area?
<number>

## Slide 12: Create a RTN Rover Check-in Mark
Notes: Lastly…here is an example of an Oregon RTN Check-In Mark Form that anyone could use to create a mark either on a project or at the office where crew members using rovers can check into a mark before work and at the end of the day to confirm alignment with the RTN and it’s coordinate system.
By their nature Check-In marks need to have better (…more accurate and true) coordinates than what might be expected say for a project kinematic control point.
In this example ODOT case, marks are created in Step 1. by taking the average of 4 – 8 minute RTK observations each separated by 30 minutes. Then in Step 2. observers log a minimum of 4 hours of static GNSS data and then publish the mark to the OPUS Database. Both may be done simultaneously if the rover data collector contains a survey configuration set that allows RTK + data logging. Publishing the Check-In mark to OPUS provides an independent solution accuracy check and verifies the check-in alignment with National Spatial Reference System.
Obviously, only marks with good stable monuments and open masks should be used as a Check-In Mark. While this particular process of creating a Check-In mark takes about a half day to complete, users report great confidence and satisfaction by checking into a reliable mark on a daily basis and they are continually assured repeatable alignment day after day using each rover with the RTN.
So far… the results of all check-in marks submitted show a difference between the 32 minutes of RTK spread over 2+ hours vs. the OPUS 4 hour solution (truth) of less than or equal to 1 cm horizontally and 1.5 cm vertically. If you would like to download this pdf fillable form as an example there is a link in the slide, on the left side at the top of the form.
<number>

## Slide 13: Questions
For further reading see the ‘NGS Real Time Network Guidelines’ and NGS User Guidelines for Single Base RT GNSS Positioning
http://www.geodesy.noaa.gov/web/news/Draft_RealTime_Network_Guide.shtml
http://www.geodesy.noaa.gov/PUBS_LIB/NGSRealTimeUserGuidelines.v2.1.pdf
Notes: This is my last slide. At the end of all the presentations today you will have the opportunity to ask questions during the last half hour of the webinar. For further reading both the “Real Time Network Guidelines” and the “Guidelines for Single Base Real Time GNSS Positioning” may be helpful.
Thank You. Okay..back to Erika to switch to the next presenter…
<number>