## Slide 1: Real Time Network (RTN) Operations
Users and Operators Perspective

## Slide 2: RTN Administration
Efficiently operates the various components of the network
  Receivers/antennas
  Servers
  Communication networks
Provides users with the information needed to utilize the network

## Slide 3: RTN Administration
Resources
  Hardware infrastructure
  Communication networks
  CORS
People
  Users
  Administration staff to provide
    Helpful support to users
    Partnership with IT professionals

## Slide 4: RTN Administration
Key component of administration staff is the system administrator
  Operates and maintains the RTN computer network
  Distributes the GNSS information to the network’s users in an efficient manner

## Slide 5: RTN Administration
Administrator abilities
  Support and maintain computer servers and communication links
  Ability to respond to service outages
    User reported problems
    Network problems
  Helpful to have a background in geodesy and satellite positioning

## Slide 6: RTN Administration
  IT Partners
    IT security
    Firewall issues
    Lightning protection
    Power system backup

## Slide 7: RTN Operations
Reference Station Datum
  Benefits of using a reference datum that is consistent with the datum used by NGS:
    Easy to verify
    Consistent with National CORS
    Can use OPUS to position RTN CORS

## Slide 8: RTN Operations
Reference Station Datum
  Ramifications of using a datum that differs from the datum utilized by NGS
    OPUS and RTN solutions would be based on different reference datums:
      OPUS could not be used to check RTN solutions
      RTN could not be used to check OPUS solutions
    Could create confusion with users

## Slide 9: RTN Operations
Connection to NSRS
  The minimum number of National CORS sites in the RTN should be the larger of the following two figures: 3 sites or 10% of the sites
  Recommend local static surveys be performed to connect RTN CORS with local NSRS passive stations

## Slide 10: RTN Operations
Connection to NAVD88
    Should be completed before the CORS antenna is installed
    May be completed afterwards if an offset leveling plate had been installed immediately below the antenna
  Field techniques
    Geodetic leveling
    Trigonometric leveling
    NGS -58 survey

## Slide 11: Questions?
Mailing address: | Building (shipping) address:
Gary W. Thompson, PLS NC Geodetic Survey 4298 Mail Service Center Raleigh, NC 27699-4298 | Gary W. Thompson, PLS NC Geodetic Survey Bowers Building NC National Guard complex 4105 Reedy Creek Rd Raleigh, NC 27607
Gary W. Thompson, PLS Office: 919-733-3836 Direct: 919-948-7844 Email: gary.thompson@ncdps.gov