## Slide 1: National Spatial Reference System Modernization
Sanborn
May 21, 2024
Brian Shaw
brian.shaw@noaa.gov

## Slide 2
Brian Shaw
Rocky Mountain Advisor
brian.shaw@noaa.gov

## Slide 3
NSRS Modernization Delay
https://geodesy.noaa.gov/datums/newdatums/delayed-release.shtml
https://geodesy.noaa.gov/datums/newdatums/FAQNewDatums.shtml
Operational, workforce retention and other issues have delayed NSRS Modernization
SPCS2022 zones will be finalized in 2024 but will not be rolled out until all of the NSRS is modernized.
Beta rollout planned for 2025, full rollout in 2026
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 4: Importance of Coordination
39 Coordinators
14 Advisors
Notes: NGS Regional Geodetic Advisors
https://geodesy.noaa.gov/ADVISORS/
State Geodetic Coordinators
https://geodesy.noaa.gov/ADVISORS/state-geodetic-coordinators.shtml

## Slide 5: NGS Resources
NGS Training Center
  https://geodesy.noaa.gov/web/science_edu/training/
Educational Videos
  https://geodesy.noaa.gov/datums/newdatums/WatchVideos.shtml
NGS Webinar Series
  https://geodesy.noaa.gov/web/science_edu/webinar_series/
Geospatial Summit (2021, 2019 recorded sessions)
  https://geodesy.noaa.gov/geospatial-summit/
Presentation Library
  https://geodesy.noaa.gov/web/science_edu/presentations_library/

## Slide 6: NGS Resources – Educational Videos
  https://geodesy.noaa.gov/datums/newdatums/WatchVideos.shtml

## Slide 7: NGS Resources – Online Lessons
  https://geodesy.noaa.gov/web/science_edu/online_lessons/index.shtml

## Slide 8: NOAA and NGS Our Nation’s First Civilian Science Agency
1807
Thomas Jefferson
Survey of the Coast
1811
Ferdinand Hassler
Superintendent
1836
U.S. Coast
Survey
1878
U.S. Coast and
Geodetic Survey
1970
NOAA is established
Notes: NGS has been around a long time. For more than 200 years, NGS and its predecessor agencies have collaborated with public and private organizations to establish reference stations at precisely determined locations.
We began on a mission established by Thomas Jefferson in 1807 to conduct a “Survey of the Coast” (as the United States Coast Survey).
(Pictured are Thomas Jefferson and Ferdinand Hassler, the first Superintendent of the Coast Survey). We were renamed the U.S. Coast and Geodetic Survey in 1878. NOAA was established in 1970.
Traditionally, precise positioning locations have been identified by setting a survey mark—usually a brass, bronze, or aluminum disk. Locations might also be identified by a deeply driven rod, or a prominent object, such as a water tower or church spire.

## Slide 9: NGS’s Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
…………………………………………….........................
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, orientation, and shoreline throughout the United States.
Sectors that Rely on Geodesy
Land
Surveying
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 10: NGS’s Historical Horizontal Networks
http://www.geodesy.noaa.gov/PUBS_LIB/NADof1983.pdf
US Standard Datum 1900
North American Datum of 1927 (NAD 27)

## Slide 11: 1983 Control Networks
Status of Horizontal Control 1983
Status of Vertical Control 1983

## Slide 12: The Bilby Tower

## Slide 14: The Importance of Geodesy
1816-1817
1969
Today

## Slide 15: The Earth is Infinitely Complex
Build Models to Simplify
Notes: Models are used to simplify complex phenomena for humans and computers to understand and perform calculations and analysis.
The geoid is an approximation of sea level and used to calculate elevations (orthometric heights) above this “sea level” surface
Spheroid image https://www.kisspng.com/png-sphere-shape-ball-grid-line-circle-draw-5378189/
Ellipsoid image https://www.kisspng.com/png-figure-of-the-earth-oblate-spheroid-ellipsoid-4129812/
Geoid Image https://www.reddit.com/r/MapPorn/comments/3xf6a0/geoid_height_of_new_global_gravity_field_models/

## Slide 16: Datums and Reference Frames
A reference surface or framework to reference your data to for consistency
aka P(Lat,Lon,Ht)
= lat.
= long.
= ht.
X,Y,Z vs Lat, Lon, Ht
60”, 2019
52”, 2018
46”, 2017

## Slide 17: Gravity is Fundamental
Aristotle (350BC)
Objects fall proportional to mass
Al-Khazini (1121)
Gravitational potential energy
Galileo (1590)
Terminal velocity
Newton (1687)
Gravity inverse-square law
Einstein (1913)
Theory of general relativity
Notes: Galileo graphic https://commons.wikimedia.org/wiki/File:GalilEXP.jpg
Spacetime curvature graphic https://www.nasa.gov/mission_pages/gpb/gpb_012.html
Aristotle (384–322 BCE)
Objects fall at a speed proportional to their mass.
The Aristotelian explanation of gravity is that all bodies move toward their natural place. For the elements earth and water, that place is the center of the (geocentric) universe;
al-Khazini (11th to 12th centuries)
In 1121, al-Khazini, in The Book of the Balance of Wisdom, proposed that the gravity and gravitational potential energy of a body varies depending on its distance from the centre of the Earth.
Galileo Galilei (1564-1642)
Leaning Tower of Pisa Experiment (1589-92) - Law of Falling Bodies
Objects fall at the same speed, independent of their mass or shape
Isaac Newton (1643-1727)
In 1687, English mathematician Sir Isaac Newton published Principia, which hypothesizes the inverse-square law of universal gravitation.
Albert Einstein (1879-1955)
Between 1911-1915 Einstein developed the theory of general relativity. In general relativity, the effects of gravitation are ascribed to spacetime curvature instead of to a force. To deal with this difficulty, Einstein proposed that spacetime is curved by matter, and that free-falling objects are moving along locally straight paths in curved spacetime. (This type of path is called a geodesic).

## Slide 18: Gravity of the Redefinition of the American Vertical Datum
GRAV-D
100% Complete (12/2023)
Notes: More information on GRAV-D
https://geodesy.noaa.gov/GRAV-D/
Data Download for GRAV-D blocks
https://geodesy.noaa.gov/GRAV-D/data_products.shtml

## Slide 19: Why Modernize the NSRS
Current models built on old technology
  NAD 83 not truly Geocentric (~2.2m)
  NAVD 88 relies on marks in the ground
  and is not easily maintained
  Today’s technology needs better accuracy
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 20: Main Benefits of Modernized NSRS
Fast, Accurate, Consistent Elevations Everywhere
Improved Public Safety
  Flood Plain Maps
  Emergency Route Planning
Accurate Positioning
  Autonomous vehicles, BIMs, Smart Cities
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 21: Best ways to determine coordinates in Modernized NSRS
Resurvey: Return to the field and collect new observations, relying upon geodetic control that has coordinates in the new datum
Readjust: Using existing observations, re-compute new coordinates based upon geodetic control (CORS) that has been defined in the new datum
Transform: Take finished products which have coordinates in the old datum and use transformation software to estimate coordinates in the new datum

## Slide 22: Preparing for the Modernized NSRS
For all control points and checkpoints, store the raw observation data files (for example, RINEX observation files), so that they can be reprocessed later relative to the modernized NSRS
For all data deliverables (and possibly important intermediate products), store versions with geodetic coordinates (latitudes, longitudes, and ellipsoid heights) relative to the current NSRS (e.g., NAD 83(2011) epoch 2010.00), even if the project deliverables call for, say, SPCS83 northings, eastings, and NAVD88 heights.
Ensure that all metadata for all archived data (not just final deliverables) is complete and correct wrt reference frames, coordinate epochs, units, geoid models applied (e.g., GEOID18), and acquisition dates.
Document project workflows with particular attention to any coordinate transformations
Work with software manufacturers for all steps in your end-to-end project workflow to ensure they are aware of and preparing for NSRS modernization

## Slide 23: Preparing for the Modernized NSRS
Metadata about the datums and geoid used will be essential.
LiDar – NGS processes everything to the ellipsoid. This enables different geoid models to be applied and will make it easier to transform products to the Modernized NSRS rather than from NAVD88.
GCPs – if you keep the original occupations you can process them in the Modernized NSRS and then align the data into the new system.

## Slide 24: Preparing for the Modernized NSRS
Digital Coast : Users can select geoid to get NAVD88

## Slide 25: The Future Reference Frames
Tectonic Plate based
Each Plate is based on the same
densified ITRF model
North America NATRF
Caribbean CATRF
Pacific PATRF
Mariana MATRF
The tectonic plates “fixed” for the
2022 Terrestrial Reference Frames
NATRF2022
PATRF2022
MATRF2022
CATRF2022
Notes: NSRS Modernization Naming Conventions https://geodesy.noaa.gov/datums/newdatums/naming-convention.shtml

## Slide 26: NAPGD2022 Geopotential Datum
North American-Pacific Geopotential Datum of 2022
Models included: Geopotential Deflection Gravity
Geoid
Guam/CNMI
American Samoa
¼ Earth’s Surface
Not a vertical datum, it is more than just heights.
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml
Experimental Geoid Models
https://beta.ngs.noaa.gov/GEOID/xGEOID20/
As noted in the Blueprint 2 document
https://geodesy.noaa.gov/library/pdfs/NOAA_TR_NOS_NGS_0064.pdf
NAPGD2022 will include all of the following
Geopotential Model of 2022 (GM2022) will include:
Static Geopotential model of 2022 (SGM2022)
Dynamic Geopotential model of 2022 (DGM2022)
GEOID2022 will include:
Static Geoid model of 2022 (SGEOID2022)
Dynamic Geoid model of 2022 (DGEOID2022)
DEFLEC2022 will include:
Static Deflection of the Vertical model of 2022 (SDEFLEC2022)
Dynamic Deflection of the Vertical model of 2022 (DDEFLEC2022)
GRAV2022
Static Gravity model of 2022 (SGRAV2022)

## Slide 27: NSRS Modernization Catch Phrase
Shift and Drift
Not the Fast and Furious

## Slide 28: Shift and Drift
A sudden shift
  Horizontal change: 0.5 to 4 m (1.5 to 13 ft)
  Ellipsoid height change: ±2 m (±6 ft)
  Elevation change: -0.5 to +2 m (-1.5 to +6 ft)
A continuous drift
  Coordinates associated with specific dates
Two components of drift:
  Tectonic plate rotation (easy to model, 2D only)
  All other residual motion (hard to model, 3D)
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 29: Shift: datum changes
~1 to 1.5 meters North America
~2.5 to 4 meters in Pacific
0 to 1.3 meters CONUS
Notes: New Datums What to expect https://geodesy.noaa.gov/datums/newdatums/WhatToExpect.shtml
NGS is not shifting the land, merely shifting the reference surfaces to which we reference the geospatial data to.

## Slide 30: Drift: Plate Tectonics and Velocities
Annual changes to
ITRF2014 coordinates
Notes: All plates are moving and through the constant collection of GNSS data using CORS we can now model where the land is moving. In the center of tectonic plates there is generally motion that can be measured but where plates converge can be thought of as a crunch zone and the modeling has much more uncertainty due to geophysical phenomena.

## Slide 31: Continuously Operating Reference Stations
P033
Ten Sleep
Wyoming
CTMC
Golden
Colorado

## Slide 32: Vertical Motion
Subsidence
  Ground fluid withdrawal, sedimentation
Glacial Isostatic Adjustment (GIA)
  Crustal rebound from glaciers (uplift)
Geophysical Phenomena
  Earthquakes, calderas, Earth tides

## Slide 33: Vertical Motion
8.5 meters
50 years
San Joaquin Subsiding
20-24” in 16 months
May 2015
to
Sept 2016
Hudson Bay Uplifting
8 -13 mm/year
Notes: San Joaquin Subsidence article
http://www.digitaljournal.com/tech-and-science/technology/sinking-san-joaquin-valley-of-california-seen-from-space/article/487393
Hudson Bay Uplift article (GIA)
https://www.researchgate.net/figure/Contour-map-of-observed-CBN-vertical-rates-Preliminary-results-from-the-combination-of_fig3_286867540
Photo of San Joaquin Valley Subsidence to 1977
https://lh4.googleusercontent.com/ymKsoXwZEP4rk4F4GqPD5S9FyMO4d0mrfL2GiLI0mXe7djBwYH3t0-OwncYltY8OJNmYk0DKh4pOLqS9DGItCHK3i23maqpjdDDISQH5ux0uqDVbrEnWTnFLPb7Woe2cka61EXC6

## Slide 34: Horizontal and Vertical Motion - Earthquakes
2020 Puerto Rico
16 cm Vertically
2019 China Lake, CA
6-10 feet Horizontally
Notes: China Lake Earthquake
https://www.usgs.gov/news/update-magnitude-71-earthquake-southern-california?qt-news_science_products=7#qt-news_science_products
Puerto Rico Earthquake
https://cunycis.maps.arcgis.com/apps/webappviewer/index.html?id=5f516f41baa84f9ba9e8207c2005ee4d

## Slide 35: GPS on Bench Marks
Web Map Application
Dashboard
~3,400 Completed in 2020
~4,900 Completed in 2021
~2,500 Completed in 2022
~2,100 Completed in 2023
Notes: China Lake Earthquake
https://www.usgs.gov/news/update-magnitude-71-earthquake-southern-california?qt-news_science_products=7#qt-news_science_products
Puerto Rico Earthquake
https://cunycis.maps.arcgis.com/apps/webappviewer/index.html?id=5f516f41baa84f9ba9e8207c2005ee4d

## Slide 36: OPUS Shared Solutions Dashboard
Agency type | # Shared Solutions on NGS marks
State | ~44,900
Private Sector | ~7,900
Federal | ~4,700
Academic | ~1,800
2018
2020
2021
Note the impact of GPSonBM Campaigns
Dashboard enables sorting and visualization of Shared Solutions by
Month & Year, State, Agency Type, and submitting agency

## Slide 37: NGS Mark Recovery Webpage
Crowd sourced mark recoveries help update the GPSonBM map, let NGS and others know if the mark is still usable, and pictures make it easier to find.
https://geodesy.noaa.gov/surveys/mark-recovery
Now with Find Marks Near Me!
Maintain your local control network: Submit a Recovery Note for each mark you find (up to once per year)
Did you find it?
Is it GPSable?
Got new photos?

## Slide 38: National Adjustments
Geometric (approximate numbers)
    Projects: ~5,300
    Stations: ~107,000
    Vectors : ~446,000

## Slide 39: National Adjustments
Orthometric (approximate numbers)
  USA
    Projects : ~23,900
    Stations : ~1M
    Observations : ~2.1M
  Canada
    Projects : ~2,900
    Stations : ~177,000
    Observations : ~204,000

## Slide 40
https://geodesy.noaa.gov/SPCS/
State Plane Coordinate System of 2022 (CONUS, Alaska and Hawaii)
Three territory zones not shown:
Puerto Rico and U.S Virgin Islands
  American Samoa
  Guam and Commonwealth of the Northern Mariana Islands

## Slide 41
CO SPCS 2022
https://geodesy.noaa.gov/SPCS/
Notes: Rocky Mountain Coordinate Reference System Handbook
https://www.marls.com/wp-content/uploads/2022/02/RMCRS-Manual-v2.0.pdf

## Slide 42
CO SPCS2022 Experience
https://experience.arcgis.com/experience/dddb7bc0be6f4e56a1c370c8d529d1a0
1 Statewide Zone
35 LDPs
Notes: Rocky Mountain Coordinate Reference System Handbook
https://www.marls.com/wp-content/uploads/2022/02/RMCRS-Manual-v2.0.pdf

## Slide 43
SPCS2022 Experience
https://experience.arcgis.com/experience/dddb7bc0be6f4e56a1c370c8d529d1a0
Notes: Rocky Mountain Coordinate Reference System Handbook
https://www.marls.com/wp-content/uploads/2022/02/RMCRS-Manual-v2.0.pdf

## Slide 44: Newish NGS Map
https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=190385f9aadb4cf1b0dd8759893032db
Notes: https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=190385f9aadb4cf1b0dd8759893032db

## Slide 45: Newish NGS Map
https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=190385f9aadb4cf1b0dd8759893032db
Share widget – shares location
https://arcg.is/1zybir
Notes: https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=190385f9aadb4cf1b0dd8759893032db

## Slide 46: NGS ArcGIS Online Resources
NGS Datasheets
NOAA CORS Network
GPS on Benchmarks Priority List
(4 layers - marks, hexagons)
GEOID18 GPS on Benchmarks
GEOID12B GPS on Benchmarks
OPUS Shared Solutions
Mark Recoveries Submitted to NGS
Feature Services
Raster Tile Services
GEOID18 Height (CONUS, PRVI)
GEOID18 Difference (CONUS, PRVI)
GEOID18 Uncertainty (CONUS, PRVI)
GEOID18 Improvements (CONUS, PRVI)

## Slide 47: Passive Marks Page
Notes: https://geodesy.noaa.gov/datasheets/passive-marks/index.html

## Slide 48: OPUS-Projects 5.2 for RTN/RTK Vectors
NGS is developing a new Standardized GNSS Vector EXchange Format (GVX) that will be used to ingest vectors into OPUS Projects

## Slide 49: OPUS-Projects 5.2 for RTN/RTK Vectors

## Slide 50: Questions?
Brian Shaw
brian.shaw@noaa.gov
Magnitude of the Deflection of the Vertical