## Slide 1: Latest Advancements at the National Geodetic Survey
January 25, 2011
TRB 90th Annual Meeting
Ronnie Taylor
Acting Director, NGS

## Slide 2: Evolving Infrastructure
OLD
Data is Submitted Via the Complex “Bluebook” Process
Individual Systems Manually Linked by Users
GPS CORS
NEW
Submit GPS Data to NGS  Stored using OPUS DB, in a New NGS Database
VDatum: Transforms Geospatial Data from Different Sources into a Common System.
GNSS CORS

## Slide 3: Modernization
New Geopotential “Vertical” Datum
  2022 estimated completion
  Defined by combination of GNSS and gravity data
  GRAV-D working in AK and CA
  FY11 target is 13%
New Geometric “Horizontal” Datum
  2022 estimated completion
  Primary access through GNSS technology and active control (CORS) instead of passive marks
Notes: <number>

## Slide 4: VDatum: Vertical Datum Transformation tool
Allows transformation of a single point or many points from one vertical datum to another
Supports vertical datum transformations for placement into three categories;
  Ellipsoidal
  Orthometric
  Tidal
http://vdatum.noaa.gov/

## Slide 5
Data Collection Update:
Current: PC-12 survey in CA for Jan-Feb, then 7 months of flying aboard leased aircraft in AK. Return to PC-12 in Sept 2011.
GPRA: 7.83% of total area was measured by end of FY10. As of Nov FY11, we upped the total to 9.05% coverage, toward a cumulative goal of 13% (stretch 15%) at end of FY11.
Data Processing Update:
Software: In-house airborne gravity software is working. Java interface is in development.
2022 Targets:
Orthometric heights good to 2 cm anywhere, anytime from GNSS technology
Height changes easily monitored using new vertical datum
GRAV-D Program:
Gravity for the Re-definition of the American Vertical Datum
2008 and 2009 Surveys
2010
2011
2011
2011
2011
http://www.ngs.noaa.gov/GRAV-D/
Notes: <number>

## Slide 6: CORS Program
1,656 Stations
Added ~210 (green dots)
in FY 2009-2010
In FY11 NGS will:
  Install 1 foundation CORS to support improvement of ITRF
  Install 3 CORS co-located with tide/water level stations
CORS Network
November 2010:
http://www.ngs.noaa.gov/CORS/
Notes: <number>

## Slide 7: OPUS - Projects
Web-based access to tools for projects involving multiple sites and occupations
  Data uploading through OPUS
  Customizable data processing via the PAGES software suite
  Visualization and management aids
  Review repeat measurements
  Network adjustment with GPSCOM
  Publish in NGS Integrated Data Base

## Slide 8: LOCUS
Leveling Online Computation User Service
Online geodetic leveling processing tool which will allow user to adjust geodetic leveling projects and return coordinates, thus allowing a user access to the NSRS
Serves similar function as OPUS does for GNSS
Currently in Beta testing stage

## Slide 9: Height Modernization Program
International Great Lakes Datum (IGLD)
  Field Observations completed in August, processing underway
  Will use OPUS Projects and compare results with both NGS and Canadian adjustments
Southern Louisiana Height Modernization Project
  Observations completed, mid-October
  Included volunteer participation from Parishes
  Processing will be done by OAD
  Discussions underway for model to publish datasheets
Gage Datum Updates (ongoing)
  USGS stream gages – update NGVD 29 to NAVD 88
  Collaboration with NC and MO includes Statewide HM GPS survey by MoDNR
  Coastal water level gages - USACE, USGS, and NOAA (NGS and CO-OPS) work group update geodetic datums and tie to tidal Datums
Notes: <number>

## Slide 10: Aeronautical Survey Program
In FY11 NGS will:
Review 154 Surveys for WAAS Program (Phase 7 Project) to be delivered to FAA by 06/30/2011
Review 171 Surveys for WAAS Program (Phase 8 Project) to be delivered to FAA by 12/2010
Review 164 Surveys for WAAS Program (Phase 9 Project) to be delivered to FAA by 3/31/2011
Develop a strategic plan for the Airport Survey Program (internal?)
Notes: <number>

## Slide 11: Project Managers for new Datums
Mark Eckl – Geopotential datum
mark.eckl@noaa.gov
301-713-3176 x117
Joe Evjen – Geometric datum
joe.evjen@noaa.gov
301-713-3194 x109