## Slide 1: Geodesy for the Geographer Replacing NAD 83
URISA GIS-Pro
October 2023
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 2: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
Notes: -We are the Federal Government’s oldest scientific agency.
-part of the Executive Branch
-I know it can seem kind of strange that NGS is part of the NOS, but the origins of NGS lie with the C&GS.
-we are a “Program Office” of the NOS
Survey of the Coast – 1807
Coast Survey – 1836
Coast and Geodetic Survey – 1878
NGS since 1970

## Slide 3: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
≠
We’re not USGS, we’re NGS
Notes: -as you can read my slide, I like to point that out because over my 2 years at NGS I’ve seen and heard this misunderstanding quite a bit
-don’t worry! it doesn’t offend us! and we do work closely with USGS, but we are separate agencies within totally different departments of the federal government

## Slide 4: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
NSRS
Notes: NGS develops and maintains the National Spatial Reference System, a national coordinate system that provides the foundation for transportation, navigation, land record systems, mapping and charting efforts, and a multitude of scientific and engineering applications
CLICK
You’ve all seen this or some similar graphic I’m sure. That bottom layer… that’s our baby, the NSRS.

## Slide 5: Modernizing the NSRS
Updating all NSRS coordinates
  Replace existing datums with new datums
  Replacing existing SPCS83 with new SPCS2022
  Accounting for coordinates changing with time
Improving NGS products and services
Simplifying customer contributions
Making the NSRS:
  More accurate
  More accessible
  More efficient
Rollout in
2025

## Slide 6: What’s going to stay the same?
  NSRS Modernization
What’s going to be different?
Notes: -so you’ve probably seen that phrase that I have front and center here, NSRS Modernization
-that’s the blanket term we use to refer to not just the new datums but other updates

## Slide 7
National Spatial Reference System
A common and consistent geospatial framework to meet the economic, social, and environmental positioning needs of our Nation.
Foundational elements include:
Latitude
Longitude
Height
Gravity
Shoreline Position
…how these change over time
Horizontal Datums | Vertical Datums
NAD83 | NAVD88
NAD27 | NGVD29
Great Lakes Datums | Geoid Models
IGLD85 | GEOID18
IGLD55 | GEOID12B
Elevation
Horizontal Datums | Vertical Datums
Great Lakes Datums | Geoid Models
Notes: The primary mission of NGS is, “to define, maintain, and provide access to the NSRS to meet our nations economic, social, and environmental needs”.
NSRS is a consistent geospatial framework, common to all Federal agencies and other users
NSRS supports informed decision-making for mapping and charting, navigation, flood risk determination, transportation, land management, and more
Elements of NSRS include (but are not limited to): latitude, longitude, elevation, gravity, shoreline position + their changes over time …other elements include scale, earth orientation parameters and others
The vertical component of the NSRS currently utilizes the North American Vertical Datum of 1988 (NAVD88)

## Slide 8
Positional Components of
the NSRS
Geometric
aka “Horizontal”
Latitude, Longitude, Ellipsoid Height
Geopotential
aka Orthometric Height
aka “Elevation”
NAD83
NAVD88
Notes: -geometric component is latitude, longitude, and ellipsoid height
-geopotential component is combined with the geometric components to calculate an ortho height or capital H

## Slide 9
North American Datum
of 1983
NAD83
will be replaced by

## Slide 10
North American Terrestrial Reference Frame of 2022
NATRF2022
(pronounced: nat-ref)

## Slide 11
Notes: -what’s the Magnitude of Horizontal Change?
-we will have tools online to simplify the process of estimating NAD83NATRF2022
-see the 1.1 and 1.2m contour lines are south and just thru southern WV, so you’ll see a northwesterly shift of less than 4 feet throughout WV, between 3.7 and 3.7 feet

## Slide 13
Existing, accepted terminology
  International TRF
  first realization of the ITRF was 1992
  NATRF2022 will be based on ITRF2020
Horizontal Datum – misnomer for NAD83
Terrestrial Reference Frame?
Notes: -Where do you see an Epoch right now in NGS data?
CLICK
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 14
Watch the grid!
ITRF concept
Drift…
Epoch:
Notes: Ok, now ITRF mentioned a couple slides ago.
Most simplistic way to explain ITRF is to watch this animation.
This is a very loose representation/visualization of what the ITRF is, a characterization only.

## Slide 15
NATRF2022
North American Terrestrial Reference Frame of 2022
will replace
NAD83
North American Datum of 1983
Technically, not just NATRF2022 but also its 4 sister TRFs…

## Slide 16: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 17: Plate-Fixed NSRS TRFs
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)
Notes: We say “NATRF2022” is “fixed” to the N.A. Plate, making it a “plate fixed” frame
-the frame is constant to itself, but rotating within ITRF, and moving in a different direction than the other 3 frames

## Slide 18
ITRF – constant frame, rotating plate

## Slide 19: Plate-Fixed
NATRF – rotating frame, constant with plate

## Slide 20
ITRF or NATRF – your choice if you know epoch
if you know epoch

## Slide 21
Conversion
    change the type of coordinate
    NAD83(2011) latitude & longitude  NAD83(2011) SPCS
  Transformation
    change the datum of coordinate
    NGVD29 height  NAVD88 height
    NAD 27 latitude & longitude  NAD 83(2011) latitude & longitude
Propagation
    change the epoch of coordinate
    NATRF2022 epoch 2020.00 to NATRF2022 epoch 2023.243
Terminology - Changing Coordinates
Notes: Historically NGS has been inconsistent with these top two words.
Going forward, we will use them as:
  Conversion: Meaning to change the type of coordinate without changing the datum or frame
  Transformation: Meaning to change the datum or frame, without changing the type of coordinate

## Slide 22
Estimated Geometric Change - Horizontal
NAD83 (2011)  NATRF2022
3.6 ft
4.3 ft
3.9 ft
Direction of Shift
4.6 ft
3.0 ft
Notes: What’s the magnitude of the horizontal datum shift across Pennsylvania?
Minimum Shift ~3.75 feet
Maximum Shift ~3.97
Remember this is just an estimation, don’t hold me to the numbers please

## Slide 23: Remember…
  What’s the goal of NATRF2022?
    Give you the stability in positions that you expect
  That’s the point of Reference Epochs (REs)
    Akin to the different realizations of NAD83
    REs will be published every 5 or 10 years
      you choose when you update
      we expect many users will adopt our first Reference Epoch Coordinates (RECs), then stay there long term
aka versions
Notes: REs will be published every 5 or 10 years
-you choose when you update
-in a perfect world, everyone would stay current, but we expect many users will adopt first RE and stay ther

## Slide 24: Preparing for New Datums
  Two factors will dictate your frequency of coordinate updates
    Your accuracy needs
    The region you work in  tectonic motion
      Do manholes need cm-level updates annually?
      We accommodate that… you choose
      Just because we’re chasing the millimeter… it doesn’t mean you need to.
Notes: What’s the goal of the way NATRF2022 was designed, by including EPP2022 and IFVM2022
For a database of features in PA
Does a database of manholes in PA need cm-level coordinate updates on an annual basis? Probably not.

## Slide 25: Preparing for New Datums
  Know the epoch of your data/datasets
    consider how you will track this
      full to-the-second timestamp on every feature?
      labeling a year for each dataset?
      something in-between that works for your needs?

## Slide 26: Preparing for New Datums
  Reprocessing your data
    in a perfect world, everyone would reprocess
      What does this really mean?
        consider a hydro-enforced DEM
          start over with the raw flight data (GNSS/IMU)
          generate new point clouds
          recreate all the drainage features in new datum
      Unrealistic for vast majority
Notes:     this is totally unrealistic  both from a financial and programmatic perspective

## Slide 27: Preparing for New Datums
  Transforming your data
    NGS Coordinate Conversion and Transformation Tool
      ASCII up/download, Web Services, or Download
      Source code on GitHub  github.com/noaa-ngs
      ask your software provider(s) about integration
        we envision COTS integrations as most popular method of access
Notes: Transforming your data
NCAT - NGS Coordinate Conversion and Transformation Tool
available now: ASCII upload and Web Services
ask your software providers about integration
we envision this as most popular method of access
Industry Workshops - May 2021 and August 2022
-Esri, Trimble, Blue Marble, etc… all the well known names attended
Geospatial Software Developers’ Summit – Nov/Dec
- International & Virtual  US NGS and NRCan CGS

## Slide 28
NCAT will allow you to propagate new field data from
Survey Epoch to Reference Epoch

## Slide 29: About the timing of it all…
Timeline
  Complete review of stakeholder submittals
  Late 2022-Early 2023: Preliminary designs for stakeholder review
  Mid-2023: Finalize all zone designs
Other things in 2023
  Provide machine-readable definitions
  Modify NGS algorithms (e.g., 1-parallel Lambert)
  Document new projection algorithms
Release with rollout of modernized NSRS
  Final definitions available by late 2023
  Release with new “datums” in 2025
Rollout in
2025

## Slide 30
geodesy.noaa.gov/ADVISORS/
Regional Geodetic Advisor Program
14 RGAs across country
We are here to support:
  You
  Your constituents
  Our Federal Partners
Questions about
NSRS Modernization?
  Reach out now
  Be prepared