## Slide 1: State Plane Coordinate System of 2022 Update
The Next Generation of State Plane
Michael L. Dennis, PhD, PE, PLS
SPCS2022 Project Manager
Federal Geodetic Control Subcommittee
February 6, 2024

## Slide 2: State Plane Coordinate System of 2022 (SPCS2022)
Part of modernizing the National Spatial Reference System (NSRS)
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Same 3 conformal map projection types
  Same ellipsoid as SPCS 83 (GRS80)
Same as existing State Plane, but different…
  Based on new terrestrial reference frames instead of NAD 83
  More zones, most designed by state stakeholders
  Designed to reduce linear distortion at topographic surface (i.e., reduce difference between “grid” and “ground” distances)
Design of all SPCS2022 zones nearly done!
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 3: A brief history of the SPCS2022 project
2017
Begin SPCS2022 project: May 23

## Slide 4: A brief history of the SPCS2022 project
2017
2018
Presentation to FGCS: Feb 22
Special Publication NOS NGS 13: Mar 6
Webinar (State Plane history): Mar 8
Webinar (SPCS2022): Apr 12
Issue Federal Register Notice (FRN): Apr 18
Deadline for FRN comments: Aug 31
Presentation to FGCS (review FRN comments): Oct 25

## Slide 5: A brief history of the SPCS2022 project
2017
2018
2019
Webinar (SPCS2022): Mar 7
Publish SPCS2022 Policy and Procedures: Apr 23
Webinar (U.S. survey foot): Apr 25
Webinar (SPCS2022): May 6
Webinar (SPCS2022): Oct 10
Initial FRN on deprecation of U.S. survey foot: Oct 17
Webinar (U.S. survey foot): Dec 12

## Slide 6: A brief history of the SPCS2022 project
2017
2018
2019
2020
Stakeholder request and proposal deadline: Mar 31
Webinar (SPCS2022): June 11
Issue final determination FRN for deprecating U.S. survey foot: Oct 5

## Slide 7: A brief history of the SPCS2022 project
2017
2018
2019
2020
2021
Stakeholder design submittal deadline: Mar 31
Webinar (SPCS2022): Dec 9

## Slide 8: A brief history of the SPCS2022 project
2017
2018
2019
2020
2021
2022
Webinar (SPCS2022 and U.S. survey foot): Nov 10
U.S. survey foot deprecated: Dec 31

## Slide 9: A brief history of the SPCS2022 project
2017
2018
2019
2020
2021
2022
2023
Presentation to FGCS: Feb 7
Presentations and paper at FIG conference: May 28-31
Update SPCS2022 Policy and Procedures: Jul 1
Release preliminary SPCS2022 “alpha” website: Jul 17
Webinar (alpha SPCS2022): Jul 20

## Slide 10: A brief history of the SPCS2022 project
2017
2024
2018
2019
2020
2021
2022
2023
Last presentation to FGCS before SPCS2022 definitions are finalized:
Today!

## Slide 11: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 12: Number of SPCS2022 zones (preliminary)
Designs by NGS
  165 zones
  Includes 54 statewide zones…
  …and 3 “special use” zones (in more than one state)
Designs by state stakeholders
  802 zones in 28 states
Total = 967 zones for 56 states and territories
Compare to 125 zones in existing State Plane

## Slide 13: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio | Examples
20 ppm | 2 cm/km | 0.11 ft/mile | 1:50,000 | Typical “low distortion projection” limit
50 ppm | 5 cm/km | 0.26 ft/mile | 1:20,000 | Minimum distortion for designs by NGS
100 ppm | 10 cm/km | 0.53 ft/mile | 1:10,000 | Historic State Plane distortion design limit
400 ppm | 40 cm/km | 2.11 ft/mile | 1:2,500 | UTM distortion design limit

## Slide 14
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±370 ppm
Performance percentages:
90% population
91% cities & towns
86% total area
Mean weighted by population: -99 ppm
GREEN: grid = ground (within ±50 ppm or ±0.26 ft/mile)
Grid versus ground distance
BLUE: grid SHORTER than ground
RED: grid LONGER than ground

## Slide 15
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)

## Slide 16
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
These zones will be removed

## Slide 17
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
This zone will change, additional zones may be added

## Slide 18
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 19
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±159 ppm
Performance percentages:
90% population
85% cities & towns
59% total area
Mean weighted by population: -75 ppm

## Slide 20
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 21: Alpha products are NOT final products!
Preliminary
For illustrative purposes only
Not authoritative
Under active development
Subject to change without notice
Feedback to: ngs.feedback@noaa.gov
https://alpha.ngs.noaa.gov/index.shtml

## Slide 22: Alpha SPCS2022 Home
https://alpha.ngs.noaa.gov /SPCS/index.shtml
Gives date last updated (on all SPCS2022 pages)
Links to other SPCS2022 pages in sidebar:
  Zone information
  Distortion maps
  Online interactive maps (SPCS2022 Experience)
  Alpha NCAT
  Additional information
  Feedback

## Slide 23: Zone Information
Interactive tables
  Zone definitions
  Example coordinates
Downloadable data and other tables will be added later

## Slide 25: ArcGIS Online SPCS2022 Experience
Online interactive maps
Shows distortion and gives projection definitions

## Slide 27: NSRS Modernization
Alpha site is ONLY for NSRS Modernization
Rollout 2025
More to it than just SPCS2022…
  Deprecation of U.S. survey foot
  Terrestrial reference frames
  Geopotential datum
  Time-dependence
  Reference epoch coordinates
  And more…
PRELIMINARY

## Slide 28: That’s great, but when will SPCS2022 be done?
SPCS2022 included with rollout of Modernized NSRS in 2025
But SPCS2022 design will be done sooner
  Getting feedback from stakeholders and others NOW
  In process of finalizing designs NOW
  Updating projection algorithms NOW
Designs done and shared with the world this year (2024)!
  Provide definitions directly usable by commercial partners
  Definitions also in EPSG Geodetic Parameter Dataset and ISO Geodetic Registry
  Issue Federal Register Notice
  Plus a detailed report (or two…)

## Slide 29: Where to learn more…
geodesy.noaa.gov
Questions?
Comments?