## Slide 1
Changes are Coming
They will Impact your Mapping
geodesy.noaa.gov
ESRI SWUG
March 27, 2019
Pam Fromhertz
Rocky Mountain Regional Advisor
Pamela.Fromhertz@noaa.gov
240-988-6363
John Hunter
CO State Geomatics Coordinator
John.Hunter@denverwater.org
303.634.3519
CoCoordinator@plsc.net

## Slide 2: Agenda
Intro
NSRS Modernization
SPCS2022
  Changes are coming – what do you want for your state
  Your input is critical
GPS on BM
  Phase I - Geoid18
  Phase II – keep collecting
Resources

## Slide 3
NGS Advisors
Other NGS offices
Notes: Just a brief background of me and my agency – I am located in CO as the Rocky Mountain Regional Geodetic Advisor, for CO, WY and MT. That means I am a resource for all in my region working on geospatial issues especially as they connect to positioning, navigation, geodesy, and how things are referenced geospatially.

## Slide 4
State Coordinators
Rocky Mountain Region Coordinators

## Slide 5: Who
Members:
  Thomas Breitnauer, Denver International Airport
  Rick Corsi, Office of Information and Technology
  Annabelle Montoya, GIS Colorado, City of Wheatridge
  Joey Stone, Denver Water
  Darren Shanks, CDOT
Advisors:
  Todd Beers, President PLSC
  Pam Fromhertz, NGS Rocky Mountain Regional Advisor
  Becky Roland, PLSC Executive Secretariat
State Geomatics Coordinator:
* John Hunter, Professional Land Surveyors of Colorado (PLSC),
Denver Water
CoCoordinator@plsc.net

## Slide 7: NSRS Modernization Who and What
The National Geodetic Survey, the federal agency responsible for establishing and maintain the positioning framework to support all federal civilian mapping and charting in the United States, is modernizing the National Spatial Reference System (NSRS).
What does this mean?
  All horizontal and vertical datums in the NSRS (NAD 83, NAVD 88, etc.) will be updated with:
    Four (4) new Terrestrial Reference Frames of 2022
    North American-Pacific Geopotential Datum of 2022
  New tools, products, services, and methodologies will be developed jointly to support the transition and access to an improved, modernized NSRS.

## Slide 8: NSRS Modernization
Vastly improved flood plain mapping
Water flows due to differences in gravity
Critically important in low-lying, flat communities
Fundamental support for new technologies
“Smart Highways” for autonomous vehicles
Revolutionize professional surveying
No more need for installing and locating bench marks
Absolute, consistent positioning autonomously, anywhere
Impacts on infrastructure
Any application requiring precise positioning -- bridges, tunnels, railways, agriculture, navigation -- will be easier and more accurate

## Slide 9
All coordinates and heights
will change!
In Colorado by over 4 feet horizontally and around -2 feet vertically

## Slide 10
New geometric datum minus NAD 83 (horizontal)

## Slide 11
New geometric datum minus NAD 83 (ellipsoid height)

## Slide 12: New Vertical Datum (Outcome)

## Slide 13
HORIZONTAL = 1.3671 m (4.5 ft)
ELLIPSOID HEIGHT = - 0.87 m (-2.85 ft)
Computed with HTDP and Inverse
ORTHOMETRIC HEIGHT = - 0.35 m (-1.14 ft)
Computed with xGEOID16B
Predicated Positional Changes in 2022
Computed for S 411(KK1411) near Arvada, CO

## Slide 14: These are part of the NSRS*
Horizontal Datums and Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations and Conversions
USSD | NGVD 29 | IGLD55 | GEOID90 | NADCON
NAD 27 | NAVD 88 | IGLD85 | GEOID93 | VERTCON
NAD 83 | PRVD02 |  | ALASKA94 | 
 | ASVD02 |  | GEOID96 | SPCS 27
 | NMVD03 |  | GEOID99 | SPCS 83
 | GUVD04 |  | GEOID03 | 
 | VIVD09 |  | GEOID06 | 
 |  |  | GEOID09 | 
 |  |  | GEOID12(A,B) | 
*This not a complete list.

## Slide 15: These are not part of the NSRS*
Horizontal Datums and Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations and Conversions
WGS 84 | IHRS |  | OSU91A | CORPSCON
ITRF |  |  | EGM96 | Appendix B.6 of DMA TR 8350.2 (WGS 84)
IGS |  |  | EGM2008 | Oregon Coordinate Reference System
 |  |  |  | The Kansas Regional Coordinate System
*This is not a complete list.

## Slide 16: NCAT NGS Coordinate Conversion and Transformation Tool
Notes: We also have a new tool available to convert between various coordinate systems using various projects.

## Slide 17: SPCS2022 Zone layers and LDPs
Each state may have max of THREE zone layers:
  One layer will be statewide zone (designed by NGS)
  Other layers have two or more zones (“multi-zone”)
  Only one layer can have discontinuous coverage
Multi-zone layer can consist of LDPs:
  Designed by stakeholders
  Minimum zone width 50 km (if height range < 250m)
  LDP coverage can be discontinuous…
Notes: Layered zones are allowed for SPCS2022 (for a max of 3 layers)
  One state in SPCS 83 has 2 layers, Kentucky (statewide plus a pre-existing 2-zone layer)
  States can have 1, 2, or 3 layers
  One layer MUST be a statewide zone (so a state with 1 layer has only a statewide zone)
  The other 1 or 2 layers will almost always have multiple zones (unless a state has, say, a single LDP in SPCS2022 that covers only part of the state)
  Only 1 layer can be “discontinuous”, that is, consist of layers that do not collectively cover the entire state (will show an example of this)
Decision to go with 3 layers based on FRN responses, especially those from mountainous western states
The multi-zone layer(s) can consist of LDPs
  Almost always means distortion criterion < ±50 ppm, so must be designed by others (i.e., “contributing partners”), not by NGS

## Slide 19
Shifted central parallel south to reduce distortion range, decreased scale to reduce distortion in cities.

## Slide 20
Preliminary
Preliminary

## Slide 21
Prototype
Prototype

## Slide 22: Montana statewide
Preliminary
Notes: Map of preliminary default SPCS2022 design for Montana, which is also a statewide zone.

## Slide 23: Montana statewide + discontinuous LDPs
Preliminary
Notes: Map showing preliminary default SPCS2022 design for Montana with layer of discontinuous LDP zones
Both the statewide and LPD zones use the system distortion color ramp (±50 ppm increment)
LDP zones shown are from the existing Rocky Mountain Tribal Coordinate Reference System (RMTCRS)
If decided by Montana stakeholders, a modified (and likely augmented) version of the RMTCRS could coexist with the default statewide zone designed by NGS.

## Slide 24: GPS on Bench Marks
Phase I
  Geoid 18
  You helped with the final hybrid Geoid Model
  All About heights
  How important will heights/elevation be in the future?
Phase II
  Transformation Tools
  Help needed with the transformation tools to the new systems over the next couple of years
Thank you

## Slide 25: Ellipsoid, Geoid, and Orthometric Heights
(NAVD88) H
H = Orthometric Height (leveling)
H = h - N
TOPOGRAPHIC
SURFACE
h = Ellipsoidal Height (GPS)
N = Geoid Height (model)
h (NAD83)
Ellipsoid
N
Geoid
Geoid Height
(GEOID12B)
Heights – why so important?

## Slide 30: Next Steps
Phase II
New priority stations for Transformation tool
  Many more stations (from 30 km to 10 km spacing)
  Design a more localized approach
  Provide incentive
  Utilize interns (request positions)
  NGS is exploring use of RTK

## Slide 31: Crowdsourcing GPS on Bench Marks
Find Bench Marks (priority and others)
  Use our priority BM/tracking map
  Use NGS Data Explorer
  Use DS-World
Provide a recovery note
  Use DS-World (or new NGS beta app)
  Provide updated descriptions,
  Coordinates, photos (use DS-World)
Collect GPS data
  Share through OPUS
  Create OPUS Data Sheet
GIS Community
can assist here
Requires Survey Grade
GPS data and
min. of 4 hrs of data

## Slide 32: OPUS Share Data Sheet

## Slide 33
Mark Recovery Form
Partial Sample

## Slide 34
NGS GPS on BM Training Material
NGS Video Library
NGS Online Lessons
GPS on Bench Marks Webpages

## Slide 35: Rocky Mountain Region Map and Volunteer Sign up
Signup sheet:
https://survey123.arcgis.com/share/130be382350e4a38a71de3b2e4d92a98 (Must cut and paste)
Status Map:
https://www.arcgis.com/apps/webappviewer/index.html?id=0829616b6ec740b7a0bfbf057188e865
NGS Map:
https://geodesy.noaa.gov/GPSonBM/index.shtml

## Slide 36
geodesy.noaa.gov

## Slide 37: Resources geodesy.noaa.gov
Webinars
  SPCS2022, GPS on BM, …
Subscriptions Services
  NGS news, webinars, training, GPS on BMs
Geospatial Summit
  Register now – in person, webinars, recordings
  May 6-7, outside DC
Training, Presentations (library)

## Slide 38
Thank you
NOAA’s National Geodetic Survey
Pam Fromhertz
Rocky Mountain Regional Advisor
Pamela.Fromhertz@noaa.gov
240-988-6363
Geodesy.noaa.gov
John Hunter
CO State Geomatics Coordinator
CoCoordinator@plsc.net
John.Hunter@denverwater.org
303.634.3519