## Slide 1: NOAA Sentinel Site Program: Sea Level Rise and Coastal Inundation
Virginia Association of Surveyors Fall Seminar:
Sea Level Rise and Subsidence
September 19th, 2014
Galen Scott
National Geodetic Survey

## Slide 2: Quotes to Kickoff
"As relative sea level increases, it no longer takes a strong storm or a hurricane to cause flooding. Flooding now occurs with high tides in many locations due to climate-related sea level rise, land subsidence and the loss of natural barriers "
-Dr. William Sweet, NOAA Nusiance Flooding Study
“I don’t know many churches that have to put the tide chart on their Web site” - Rev. Jennifer Slade, Unitarian Church of Norfolk Washington Post 5/28/2014

## Slide 3: A quote of my own
“Sea level rise” or “recurrent flooding”, no matter what you call it, Hampton Roads is getting wet and understanding elevations and the relationships between tidal and geodetic datums is crucial for planning and adapting.
Image From: www.hamptonroads.com
Hurricane Isabel – September 18th, 2003

## Slide 4: NGS Mission Statement
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our nation’s economic, social, and environmental needs.
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, and orientation throughout the United States - and how these values change with time.

## Slide 5: National Spatial Reference System (NSRS)
NSRS comprises a consistent, accurate, and up-to-date national shoreline; a network of continuously operating reference stations (CORS) which supports 3-dimensional positioning activities; a network of permanently marked points, and a set of accurate models describing dynamic, geophysical processes that affect spatial measurements.

## Slide 6: The National Spatial Reference System supports
Emergency Response Imagery, Flood zones for the
National Flood Insurance Program
Federal Emergency Management Agency
Levee Safety Program to determine levee heights & positions
United States Army Corps of Engineers
NSRS gravity data for the geospatial mission of NGA
National Geospatial-Intelligence Agency
Topographic Maps and interior water data for the nation
United States Geological Survey
Nautical charts, among many other geospatial applications
National Oceanic and Atmospheric Administration
Aeronautical Data Quality Assurance
Federal Aviation Administration

## Slide 7
Notes: Traditionally, Mapping and Charting functions within NOAA have served our Commerce and Transportation requirements.

## Slide 8: NOAA’s Navigation Services Offices
National Geodetic Survey
  NSRS
  National Shoreline
Office of Coast Survey
  Bathymetry
  Nautical Charts
Center for Operational Oceanographic Products and Services
  Tides & Currents

## Slide 9
Notes: The NGS Ecosystems and Climate Operations Team applies the science and expertise that have historically served our navigation responsibilities toward new non-traditional science and management applications in the coastal zone

## Slide 10: NOAA Data, Models, and Tools for Informing Adaptation Decisions
Water level data
Geodetic Data
Geophysical data
Models
Transformation programs
GIS applications
Subsidence/Crustal Movement

## Slide 11: NOAA Coastal Operational Forecast System
Coastal ocean backbone to support navigation, hazards response, ecological
Web products used daily by coastal managers, maritime, navigation and emergency response communities.
Graphics on CO-OPS Web Site:
Water levels, currents, temperature, salinity, and surface winds at selected locations
Time series plots of selected locations, contour and vector map plots, animations
Notes: Chesapeake Bay Operational Forecast System (CBOFS)
http://tidesandcurrents.noaa.gov/ofs/cbofs/cbofs.html

## Slide 12: Chesapeake Bay Operational Forecast System – Water Levels
Notes: Chesapeake Bay OFS Water Level Nowcast
http://tidesandcurrents.noaa.gov/ofs/ofs_animation.shtml?ofsregion=cb&subdomain=0&model_type=wl_nowcast

## Slide 13
Coastal Intelligence
Planning for Long-Term Resilience
Supporting Community Livability
Ensuring Safe, Efficient, and Environmentally Sound Navigation
Promoting Resilience to Coastal Hazards and Climate Change
Building a Weather-Ready Nation
Notes: http://oceanservice.noaa.gov/
Graphics (in order): Promoting Resilience to Hazards (SLR/Coastal Inundation Impact Assessments; Extreme Water Levels and Inundation Analysis; Foundational Data for Maritime Commerce, Transportation and Community Resilience). Weather Ready Nation-Marine Weather Forecasts (including Sea Ice Forecasts)). Community Livability (Coastal Change Analysis Program (C-CAP); Socio-Economics/ Social Science Analysis: E-NOW Application). Ensuring Safe, Efficient, Environmentally Sound Navigation (PORTS® System - The U.S. Navy LPD ship, the USS New York under the Huey P. Long Bridge just north of downtown New Orleans, Mississippi River, June ‘09); E-NAV and Electronic Chart Products; Shoreline/ Precise Positioning Services.

## Slide 14: Coastal Intelligence: Foundational Data

## Slide 15: Sea Levels, Subsidence, and Height Systems
Addressing issues of spatial and temporal scale and resolution

## Slide 16: Sea Levels Overview
Challenge: Assessing and Forecasting the Impacts of Relative Sea Level Rise on Coastal Communities and Ecosystems
Sea Level is the mean level of the ocean’s surface.
Global sea level change is the spatial average over the entire ocean.
“Absolute” changes are due to actual water volume changes.
“Relative” changes are due to vertical land motion (subsidence) and hydrodynamic processes (currents)
Long-term variability is caused by climatic changes (glacial cycles), multi-year oceanic oscillations (i.e., ENSO), and from vertical land motion (i.e., subsidence and tectonic rebound)
Short-term variability is primarily from seasonal trends, atmospheric frontal activity and from the tides

## Slide 17: Global Sea Level Change

## Slide 18: Satellite Altimetry Time Series

## Slide 19: Highly variable relative sea level changes at tide stations

## Slide 20: Regional Sea Level Trends
http://tidesandcurrents.noaa.gov/sltrends

## Slide 21: Local Sea Level Trends
–
Station | Observation Length | SL Trend (mm/yr) | 95% Confidence (mm/yr)
Gloucester Point | 53 years | 3.81 | +/- 0.47
Sewell Point | 79 years | 4.44 | +/- 0.27
Portsmouth | 52 years | 3.76 | +/- 0.45
CBBT | 31 years | 6.05 | +/- 1.21
Kiptopeke | 55 years | 3.48 | +/- 0.42
Notes: http://tidesandcurrents.noaa.gov/sltrends

## Slide 22
Before 1980, the Hague, had never flooded for more than 100 hours in a year. By 2009, it was routinely flooded for 200 hours/year.
from Washington Post 5/28/2014
$318 million light-rail system — paid for primarily with federal funds -- was built at sea level
$318 million light-rail system –built at sea level

## Slide 23: Tomorrow’s Concern: Accelerating SLR
2013 US National Climate Assessment (NCA) SLR Risk-framing Scenarios

## Slide 24: Recent Reports of Note
USGS Circular 1392 - 2013
VIMS - 2010

## Slide 25
Subsidence in the area of Chesapeake Bay
1973 Report by S. Holdhal and N. Morrison
HNPT = - 0.0024
ANP6 = - 0.0016
GAIT = - 0.0004
GODE = - 0.0011
BACO = - 0.0032*
VIMS = - 0.0034*
DRV6 = - 0.0033
COVX = - 0.0016
VAGP = - 0.0027
CORB = - 0.0010
IGS08
Vertical Velocity at Selected CORS
* = Differs by more than 1 mm from
1973 estimates
VAWI = - 0.0043*
Rates of Elevation
Change (mm/yr)

## Slide 26: Level Lines in VA
Notes: From NGS hgz files

## Slide 27: Level Lines in VA – L22443 James River Loop 1971

## Slide 28
1971-1991: Subsidence
House
BM
House
BM
1971: Leveling Performed
to bench mark
1991: Published NAVD 88 height for this BM is from 1971 leveling
The published NAVD 88 height is no longer the true height for this BM-
2.8mm * 20 years = 5.6 cm (.183 feet) – NAVD88 published
2.8mm * 43 years = 12.4 cm (.406 feet) - Today
H88(published)
H88(true)
NAVD 88 zero height surface
Subsidence and Bench Mark Height
Notes: 2.8 mm/yr subsidence estimate from Hodahl and Morrison report 1973 (slide 25)

## Slide 29: Vertical Datums - 3 Height Systems A set of fundamental elevations to which other elevations are referred.
Tidal Datums (Tide Stations)
  Defined by observation of tidal variations over a specified epoch of time
    Mean Lower Low Water (MLLW)
    Mean Sea Level (MSL)
Orthometric Datums (Leveling)
  Related to the Geoid model of the Earth
  Heights from differential leveling
    North American Vertical Datum 1988 (NAVD 88)
Ellipsoidal (3-D) Datums (GPS)
  Related to an ellipsoidal model of the Earth
  Heights directly from GPS
    North American Datum 1983 (NAD 83)
    International Terrestrial Reference Frame (ITRF 08)
Notes: NAVD 88 = Official Vertical Datum for US
The North American Vertical Datum 1988 (NAVD88) is that level surface that corresponds to mean sea level at Father’s Point, Quebec, Canada during the 1960 – 1978 National Tidal Datum Epoch
A Datum is Characterized by:
A set of physical monuments and published coordinates (horizontal and/or vertical) on the monuments

## Slide 30: The ITRF
The International Earth Rotation and Reference Systems Service (IERS) is responsible for maintaining the International Terrestrial Reference Frame (ITRF).
Four Observing Systems are used to Compute ITRF:
Very Long Baseline Inteferometry (VLBI).
Satellite Laser Ranging (SLR).
Global Positioning System (GPS).
Doppler Orbitography Radiopositioning Integrated by Satellite (DORIS).

## Slide 31
VLBI
SLR
GPS
DORIS

## Slide 32: Sentinel sites

## Slide 33: What are Sentinel Sites?
Selected locations in coastal and marine environments that have the operational capacity for intensive study and sustained observations to detect and understand changes in the ecosystems they represent.
The canaries in the coal mine…
Urban Sentinel Site??

## Slide 34: Sentinel Stations
Sentinel Stations are discrete instruments and measurement platforms and sensors, within a consistent geospatial framework, that provide information and data which can be synthesized in order to provide an understanding of the ecological status and trends in physical (water level, surface elevation, etc.) and biological variables of interest, as well as knowledge of environmental state and past and present SLC impact indicators.

## Slide 35
Goodwin Island “Sentinel Site”
Notes: From Scott Lerberg – CBVA NERR
The Goodwin Islands are located at the mouth of the York River subestuary and are an archipelago of marsh islands surrounded by submerged aquatic vegetation (SAV) beds and shallow open estuarine waters. CBNERRVA with collaborators have developed the critical infrastructure and data analysis capacity to address both short-term, episodic impacts and longer-term trends in support of targeted habitat (e.g. submerged aquatic vegetation, emergent tidal marshes, and the marsh-forest ecotone) sentinel site designation; including:
• Emergent marsh and SAV transects to monitor changes in spatial distribution and community composition of vegetated habitats
• Surface Elevation Tables (SETs) co-located with vegetation transects to monitor surface elevation changes over time
• Groundwater monitoring to evaluate salt intrusion and water table and flooding dynamic
• NERRS System-Wide Monitoring Program (SWMP) water quality station tied through GPS techniques to tidal benchmarks of nearby NWLON Station
• A local geodetic control network tied to the National Spatial Reference System (NSRS and all monitoring components so measurements are collected on the same vertical datum
• Meteorological station
• Multi-decadal aerial image analysis of shoreline and vegetation community boundaries
• Local sea level and salt intrusion model
Increased understanding of physical conditions driving changes in habitat type and quality to support wetland inventories and develop strategies to increase adaptive capacity of vulnerable wetlands

## Slide 36: Sentinel Site Program Vision
Science
Service
Stewardship
Observe & Monitor
Applied Research
Models & Predictions
Spatial Analysis & Visualization
Information Transfer
Education & Outreach
Management &
Decision Making
integrating multiple parallel efforts to promote resilient coastal communities and ecosystems in the face of climate change

## Slide 37: Sentinel Site Program Mission
To improve understanding, long-range planning, and adaptation to climate change impacts focusing on sea level change and coastal inundation, in coastal communities through coordinated planning that involves NOAA trust resources such as the National Estuarine Research Reserves and National Marine Sanctuaries in partnership with federal, state and local partners within a scientifically relevant Sentinel Site Cooperative boundary.
Notes: NOAA Sentinel Site Program Report
September 30th, 2011
http://oceanservice.noaa.gov/sentinelsites/pdf/Sentinel-Site-Program.pdf

## Slide 38: Sentinel Site Cooperatives
The spatial extent for which the outputs, products, and services from all relevant Sentinel Sites and Sentinel Stations are both scientifically relevant and applicable to local management issues.
Notes: NOAA Sentinel Site Program website:
http://oceanservice.noaa.gov/sentinelsites/

## Slide 39: NOAA Sentinel Site Program (SSP): Major Components
Sentinel
Site #1
Community:
People and Infrastructure
Sentinel
Site #2
Sentinel
Site #3
Sentinel Site Cooperative: entire spatial extent
Community: socio-economic systems
Sentinel Site: Managed, protected areas
Sentinel Station: Instrument and measurement platforms
Notes: INTRODUCTION
In 2011, the National Oceanic and Atmospheric Administration (NOAA) initiated a Sentinel Site Program (SSP) to encourage federal, state and local partners to cooperatively address impacts of climate change using a place-based approach, with an initial emphasis on supporting resilience to sea level change and coastal inundation.
This program builds on the strengths of NOAA’s National Estuarine Research Reserve Systems (NERRS) Sentinel Site program.
It describes the Cooperative’s strategic and operational approach to engaging a continuum of capabilities from observations and research to application, management, and outreach to address local impacts of sea level change and inundation
Sentinel Station. Instruments and measurement stations (platforms and sensors) located within a geospatial framework, that provide information and data that can be synthesized to provide an understanding of the variables of interest.
Sentinel Site. Areas in coastal and marine environments that have the operational capacity for intensive study and sustained observations to detect and understand changes in the ecosystems they represent.
Sentinel Site Cooperative. Spatial extent for which the outputs, products, and services from all applicable Sentinel Sites are scientifically relevant and applicable to
local management issues. Cooperatives bound not only the physical and biological data, but also the socioeconomic information necessary to deliver useful products to coastal communities. Continuum from data collection and processing to outreach and management actions.

## Slide 40: National Estuarine Research Reserve System (NERRS)
Notes: 28 Reserves , protecting > 1.3 million acres of coastal and estuarine habitats representing major biogeographical regions.
As of 2014, The NERRS Sentinel Sites include the majority of the east coast reserves, three in the Gulf of Mexico, two of the four west coast reserves, and one each in the Great Lakes and Alaska.

## Slide 41
Notes: Shows Sentinel Buildout at Waquoit Bay.

## Slide 42
permanent plots
SETs
Segment
A
Segment
B
SWMP site & NOAA tide gauge
North Inlet Winyah Bay
Spartina low marsh
Mixed meadow & Salicornia
mid-marsh
Forest edge & Juncus high marsh
0.0
0.5
1.0 Km
Assess the effects of sea level on the physical and biological structure of intertidal marsh along an elevation gradient from creek bank to upland edge within the North Inlet estuary.
Notes: Project goal: Assess the effects of sea level on the physical and biological structure of intertidal marsh along an elevation gradient from creek bank to upland edge within the North Inlet estuary.
→ Quantify horizontal & vertical rates of change in response to sea level variability.
→ Understand factors regulating plant community dynamics in relation to marsh migration and upland transgression.

## Slide 43: CBSSC Sentinel Sites
Blackwater National Wildlife Refuge
Assateague Island National Seashore
Chesapeake Bay NERR (MD)
  Otter Point Creek
  Jug Bay
  Monie Bay
Chesapeake Bay NERR (VA)
  Sweet Hall Marsh
  Taskinas Creek
  Catlett Islands
  Goodwin Islands
Virginia Eastern Shore LTER
Notes: Current locations identified as sentinel sites as part of the Chesapeake Bay Sentinel Site Implementation Plan. Long term monitoring efforts are present at each location.
http://oceanservice.noaa.gov/sentinelsites/chesapeake.html

## Slide 44: Sweet Hall Marsh Chesapeake Bay VA NERR
Sweet Hall
Taskinas Creek
Catlett Island
Goodwin Islands
Four Components of Chesapeake Bay NERR in Virginia
Notes: In order to incorporate the diversity of habitats in the southern Chesapeake Bay subregion, CBVA NERR established a multi-component system along the salinity gradient of the York River estuary.
Reserve components include Sweet Hall Marsh, Taskinas Creek, Catlett Islands and the Goodwin Islands
44

## Slide 45: Chesapeake Bay Sentinel Site Cooperative
http://www.vims.edu/cbnerr/CBSSC/
 | Current Participants
Federal | NOAA, USGS, USFWS, NPS, EPA, USACE
State | MD DNR, VA DEQ
Academic | UMD, VIMS, ODU, VCU, CNU
NGO | MARACOOS, NWF, TNC, CBF
Notes: http://www.vims.edu/cbnerr/CBSSC/

## Slide 46: Chesapeake Bay Sentinel Site Cooperative
GOAL 1: Governments, NGOs, and academic institutions have greater access to more reliable and integrated ecosystem and socio-economic data.
GOAL 2: Local governments and land and natural resource managers have decision support tools to effectively prepare for, respond to, and recover from current and anticipated sea level rise and other related climate change impacts.
GOAL 3: Coastal stakeholders and the general public understand and trust information on sea level change and coastal inundation hazards, and the severity of related impacts to Chesapeake Bay habitats, ecosystems, and built environments.
Notes: Chesapeake Bay Sentinel Site Cooperative
Implementation Plan
FY13-FY18
http://www.vims.edu/cbnerr/ChesapeakeBay_SentinelSiteCooperative_IP_FY13FY17_FINAL.pdf

## Slide 47: Chesapeake Bay VA NERR
Notes: Geospatial Infrastructure Training at CBVA NERR

## Slide 48
Sea Level
Upland
Initial Wetland Surface
Bench Mark with Geodetic Control (NAVD88, etc.)
Surface Elevation Table (SET)
Tide Station
Depth of SET measurement integration
Deep Subsidence
Subsided Wetland Surface
Rise
Shallow Subsidence
Marker Horizon
Surface Accretion
Elevation Change

## Slide 49: NWLON
National Water Level Observation Network (NWLON)
A network of continuously operating tide stations that are the foundation for NOAA’s tide prediction products
The network provides:
water level
wind speed and direction
barometric pressure
air and water temperature
conductivity/temp
Notes: http://tidesandcurrents.noaa.gov/nwlon.html

## Slide 50
CORS Network
Continuously Operating Reference Stations (CORS)
A multi-purpose cooperative network providing 3-dimensional positioning
Will incorporate results from GRAV-D for increased accuracy of vertical positioning
Co-locating with other instruments increases overall knowledge
Built with partners in the public and private sectors, including state and local governments, universities, and private businesses
Notes: http://geodesy.noaa.gov/CORS/

## Slide 51
SET Technology
Surface Elevation Tables (SETs)
Portable leveling device to measure relative elevation of wetland sediments.
SETs monitor coastal land elevation relative to local sea level rise
Provides further understanding to processes leading to the formulation and maintenance of coastal elevation
Notes: The SET is a device that has been developed over the past decade to measure incremental changes in wetland and shallow water surfaces over time with respect to a bench mark that is inserted into the sediment until refusal.
The SET was developed to understand processes leading to the formation & maintenance of coastal elevation.
Land loss is an incremental thing. Satellite imagery will tell you when the wetland is lost, not what it’s doing leading up to that loss. Elevation may be lost at rates on the order of millimeters per year - Being able to measure that loss requires precise measurements over time, and under different experimental conditions.
The Surface Elevation Table, or SET, was developed in the Mississippi Delta to support investigations into the processes leading to wetland loss.
SETs were developed to allow the investigator to monitor relative changes in coastal wetland elevation.
SETs also allow one to investigate the processes leading to changes in elevation.
SETs have also been used in experimental settings, testing the effect of different treatments such as fire or fertilization on wetland elevation.

## Slide 52: CORS/SETs/Tide Stations /Benchmarks
Long Term Tide Stations
Local Sea-Level Rise 3.29 mm/yr
Survey Control Monuments
Continuously Operating (GPS) Reference Stations (CORS)
Land Elevation Trend -1.1mm/yr
Surface Elevation Tables (SETs)
Wetland elevation dynamics
Local Marsh Trajectory - 2.1mm/yr
Notes: Three observing systems all tied to a local network of high-accuracy survey control monuments

## Slide 53
NOAA Shoreline Mapping Capability
RGB
Near-IR
LIDAR Point Cloud
OVERVIEW – Applications - Future

## Slide 54
Static GPS Differential Survey
Real Time Kinematic (RTK) GPS Differential Survey
Geodetic Digital Leveling
Establish control network and monitor stability
Occupation Time: Two separate GPS constellations for 4-6 hrs each
Positioning remote points; digital elevation models
 Occupation Time: 10-30 seconds
Monitor network connections and stability
Time dependent on distance and resources
Notes: Surveying techniques used for developing Sentinel Site Geospatial Infrastructure

## Slide 55: Supporting Geospatial Infrastructure Components
Water Quality Stations
Monitoring Wells and
Transect Surface Elevations
Vegetation Plots
Erosion Pins
Notes: Biogeophysical monitoring stations that can be tied to local vertical control network

## Slide 56: Geospatial Infrastructure Guidelines
Notes: Pending release in late 2014

## Slide 57: NGS Tools & Updates

## Slide 58: Historic T-sheets
1854 Entrance to Hampton Roads
Notes: http://nosimagery.noaa.gov/images/shoreline_surveys/noaa_shoreline_surveys.kmz

## Slide 59: Historic T-Sheets

## Slide 60: Historic T-Sheets

## Slide 61: OPUS Shared Solutions
Notes: http://www.ngs.noaa.gov/OPUS/showMarks.jsp

## Slide 62: OPUS-Projects
Officially operational Jan 2014
Enhancement to OPUS-Static
Network solution of GPS data from multiple receivers and occupations
Intuitive graphical user interface
Requires attending training to get access
Notes: http://www.ngs.noaa.gov/OPUS-Projects/OpusProjects.shtml

## Slide 63: LOCUS – Leveling Online Calculation Service
Provides tools for users to submit vertical control data, either from an optical or digital instrument, perform the necessary reductions, apply the needed constraints, and compute elevations through a standard least squares adjustment process.
Notes: http://www.ngs.noaa.gov/CORS-Proxy/locus/

## Slide 64: New Datums Coming in 2022
A new geometric and a new geopotential (vertical) datum will be released together in 2022
The realization of the new datums will be through GNSS receivers
NGS will provide tools to allow for easy transformation between the new and old datums
Notes: Both datums will be released together in 2022
- NGS will provide tools to allow for easy transformation between the new and old datums
- The realization of the new datums will be through GNSS receivers
- We expect to assign values to all BMs that have GPS observations
- NGS will develop standards and specifications for how to best blend the controlled leveling survey with the new methods of accessing the datum

## Slide 65: GRAV-D: Gravity for the Redefinition of the American Vertical Datum
Nationwide airborne gravity collection essential for the definition of an improved national vertical reference system
Profound implications for GPS elevation accuracy:
national elevations with GPS to ~ 2cm
compared to as much as 2 meters today
Aerial Gravity Collection
for a new national
vertical datum
Notes: Talking points:
Oct ’07 : NGS Acquires Airborne Gravimeter
Nov ’07 : NGS Releases Final Version of the GRAV-D plan
Nov ’07 : NGS Trains Airborne Gravimeter Operators
Jan/Feb ‘08 : NGS conducts successful test flights of gravimeter along Gulf Coast
NOAA’s National Geodetic Survey (NGS) conducted test flights in Mississippi and Alabama in January, 2008 using its recently acquired airborne gravimeter in support of the Gravity for the Redefinition of the American Vertical Datum (GRAV-D) program. GRAV-D is an effort to use gravity data to re-define the vertical datum of the United States by 2017. In support of these tests, NGS also performed ground based reconnaissance in a grid that is approximately 140k north-south and 250k east-west covering southern Alabama and Mississippi. Hundreds of grid points were observed using GPS and relative gravity meters. This information will be used to "truth" the data that is collected by the airborne gravimeter.
The GRAV-D program has profound implications for all activities (inside and outside of NOAA) which rely upon accurate heights.

## Slide 66: GRAV-D: Gravity for the Redefinition of the American Vertical Datum
Enabling coastal communities to:
improve flood protection infrastructure
plan evacuation routes
model storm surge
monitor sea-level rise
monitor levee subsidence
improve flood plain maps
Notes: Talking points:
Oct ’07 : NGS Acquires Airborne Gravimeter
Nov ’07 : NGS Releases Final Version of the GRAV-D plan
Nov ’07 : NGS Trains Airborne Gravimeter Operators
Jan/Feb ‘08 : NGS conducts successful test flights of gravimeter along Gulf Coast
NOAA’s National Geodetic Survey (NGS) conducted test flights in Mississippi and Alabama in January, 2008 using its recently acquired airborne gravimeter in support of the Gravity for the Redefinition of the American Vertical Datum (GRAV-D) program. GRAV-D is an effort to use gravity data to re-define the vertical datum of the United States by 2017. In support of these tests, NGS also performed ground based reconnaissance in a grid that is approximately 140k north-south and 250k east-west covering southern Alabama and Mississippi. Hundreds of grid points were observed using GPS and relative gravity meters. This information will be used to "truth" the data that is collected by the airborne gravimeter.
The GRAV-D program has profound implications for all activities (inside and outside of NOAA) which rely upon accurate heights.

## Slide 67: Geoid 12A Accuracy map
Notes: http://www.ngs.noaa.gov/GEOID/

## Slide 68
Notes: GPS observations on Benchmarks used to create Geoid 12A

## Slide 69: Geoid 12A in VA

## Slide 70: Geoid Slope Validation Survey of 2014 (GSVS14)
Research toward new vertical datum
E-W line across Iowa
Observations began in May 2014
Includes:
  Differential leveling
  GPS
  Terrestrial gravity
  Aerial gravity
  Deflection of vertical
This is the second GSVS project
  First in 2011 in Texas (GSVS11)

## Slide 71: NGS 58/59 update project
An update for guidelines on GNSS-derived ellipsoid and orthometric heights
Two phases
  Vertical precision (FL)
  GPS bench mark Height Mod (SC)
Fieldwork done Dec 2013
Analysis of data underway
Will be used for new guidelines to replace NGS 58/59 documents

## Slide 72: NOAA Resources

## Slide 73: http://csc.noaa.gov/slr/viewer/

## Slide 74: Shallow Flood Frequency

## Slide 75: Coastal Inundation Landmark Project
Our Goal
Improve community resilience to coastal flooding by providing consistency across water level data and cultivating partnerships to successfully incorporate this data into community planning and response.
What is a Coastal Inundation Landmark?
Familiar community locations referenced to a single benchmark
These locations will be socially relevant to the community (statues, historic sites) and important to the planning process of local emergency managers and government (metro station, fire station).
Why are Coastal Inundation Landmarks Needed?
Better communication around the extent and impacts from flooding
Supporting storm surge forecasting by reporting on the ground impacts throughout a storm
Eliminating the confusion around referencing water height over ground in our storm forecasting efforts
What can this provide to our users?
Technical basis for more effective and accurate communication of water levels during nuisance flooding, storm surge inundation, and long-term sea level rise
Consistency of water level information
A frame of reference for historical events
Real-time water level data in relation to familiar locations

## Slide 76
Notes: http://tidesandcurrents.noaa.gov/publications/Technical_Report_NOS_CO-OPS_065.pdf
http://tidesandcurrents.noaa.gov/publications/NOAA_Technical_Report_NOS_COOPS_073.pdf

## Slide 77
Notes: From Dr. Billy Sweet, NOAA CO-OPS, presentation at TechSurge 2014
Available here: http://mtshamptonroads.org/mtshr/?page_id=419

## Slide 78
Notes: From Dr. Billy Sweet, NOAA CO-OPS, presentation at TechSurge 2014
Available here: http://mtshamptonroads.org/mtshr/?page_id=419

## Slide 79
Notes: From Dr. Billy Sweet, NOAA CO-OPS, presentation at TechSurge 2014
Available here: http://mtshamptonroads.org/mtshr/?page_id=419

## Slide 80: GPS on bench marks campaign
Will help improve next hybrid geoid model and conversion to new 2022 vertical datum
Can provide a time series on specific marks of interest.
Notes: Volunteers occupied leveled bench marks with GPS
Performed during GPS Week (Mar 16-22)
Record number of shared OPUS solutions