## Slide 1
Modernizing the National Spatial Reference System
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: “Modernizing the NSRS” means…
Replacing NAD 83
Replacing NAVD 88
Re-inventing Bluebooking
Improving the Geodetic Toolkit
Better Surveying Methodologies
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 3
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
May 2017
(minor update Sep 2017)
Geopotential:
Oct 2017
Bluebooking:
Apr(?) 2018

## Slide 4: Replacing the NAD 83’s
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 5: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Remove long-standing non-geocentricity of NAD 83 frames
All four : identical to IGSxx at a TBD epoch
  2020.00?
All four : differ from IGSxx by plate rotation only
  Updated Euler Pole determination for rigid plate only

## Slide 6: The TRFs
All are global frames (no “boundary”)
  This was true for the NAD 83’s also, BTW
  But each frame will rotate with one tectonic plate
    Put another way: “The frame rotates so your coordinates don’t have to”
All will have an Intra-Frame Velocity Model
  To capture any motions outside of tectonic rotation
    Residual horizontal motions
    All vertical (ellipsoid height) motions

## Slide 7
Time “t ” when
all four TRFs and the
IGS are identical.
(maybe 2020.0?)
0
MATRF2022
MATRF2022
Rotation of Mariana Plate
t=t + Dt
(“the future”)
0
t=t - Dt
(“the past”)
0
CATRF2022
CATRF2022
NATRF2022
PATRF2022
NATRF2022
PATRF2022
Rotation of Caribbean Plate
IGS frame through time
IGS frame
IGS frame
Rotation of Pacific Plate
Rotation of North American Plate
The relation of five global reference
frames through time.
Rotations are not to scale

## Slide 8
What does it mean to provide time-dependent coordinates in 5 frames?

## Slide 9: BSMK (North Dakota)

## Slide 10: BSMK (North Dakota)
Note the time-dependent coordinate in latitude in NATRF2022 is stable! That means the NATRF2022 IFVM for latitude will be ZERO for this point.
Let’s set t to 2005.0 for now…
0

## Slide 11: BSMK (North Dakota)
Similarly, the time-dependent coordinate in longitude in NATRF2022 is stable! That means the NATRF2022 IFVM for longitude will be ZERO for this point.

## Slide 12: BSMK (North Dakota)
However, in every frame, this point is subsiding! That will be captured in the ellipsoid height component of the IFVM for each frame.

## Slide 13: ICT2 (Kansas)

## Slide 14: ICT2 (Kansas)
Note the time-dependent movement of this Kansas point in latitude in NATRF2022! Such movement will be captured in the IFVM.

## Slide 15: ICT2 (Kansas)
However, in longitude, this CORS is fairly stable in NATRF2022! Still, any deviation from stability would be in the IFVM.

## Slide 16: ICT2 (Kansas)
All vertical motion is captured in the IFVM.

## Slide 17: PIN1 (S. California)

## Slide 18: PIN1 (S. California)
In latitude, S. California neither behaves like the NA plate nor the Pacific plate. Both deviations from stability will be captured in each frame’s IFVM.

## Slide 19: PIN1 (S. California)
In longitude, S. California neither behaves like the NA plate nor the Pacific plate. Both deviations from stability will be captured in each frame’s IFVM.

## Slide 20: PIN1 (S. California)
In ellipsoid height, all frames are equal and the entire signal is captured in the IFVM.

## Slide 21
Additional examples will be presented at the end if time allows

## Slide 22: Intra-frame velocity model
Note scale difference between West (10 mm/yr) and east (2 mm/yr)
Shown on this slide are CORS-implied velocities after removing the rotation of the
North American plate. NATRF2022 coordinates will change through time by these
amounts. These time-dependent changes will be captured in the IFVM.

## Slide 23: A simple IFVM model is applied…
The simplest IFVM is already available: Interpolation of 3-D velocities from CORS stations
Removing this simple IFVM resolves nearly all velocities seen in the previous slide
Eastern CONUS will largely be resolved
Western CONUS has some anomalies
NGS is engaged in research to provide the highest quality IFVM without our abilities, possibly enveloping:
  InSAR
  Geodynamic

## Slide 24: Let’s change gears…

## Slide 25: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 26: Geopotential Basics
Why isn’t this a vertical datum?
  Because it contains more than heights
    And therefore NGS wants to be accurate in its name

## Slide 27: Expected changes to orthometric heights

## Slide 28: Expected changes to orthometric heights

## Slide 29: Definitional Relationship
Time-dependencies of ellipsoid heights
are captured in the IFVM
Time-dependencies of geoid undulations
are captured in the dynamic component
of GEOID2022 (“DGEOID2022”), which
will come from the geoid monitoring
service, or GeMS.

## Slide 30: Geoid Monitoring Service
Goal: Track all changes to the geoid which would prevent 1 cm accuracy
Three aspects need to be tracked:
  Shape
  Size
  Global Sea Level Change

## Slide 31: Geoid Shape
Like “squeezing a balloon”
Large mass changes
  Influx of mantle material under Hudson Bay causing the geoid to bulge 2 mm/year
Not crustal sloughing/compression
  Not enough mass entering/leaving an area to change the geoid

## Slide 32: Geoid Size
Like “inflating a balloon”
Not likely to be an issue
  Reliant upon Earth gaining or losing enough total mass to inflate/deflate the geoid

## Slide 33: Global Sea Level Change
Like “two balloons, one inside the other, and one day I pick the inside balloon as ‘the geoid’ and the next day I pick the outside balloon as ‘the geoid’
By definition, the geoid “best fits” GMSL
But GMSL changes rapidly, and this might disrupt users
Set “threshold” value to “jump” the geoid…

## Slide 34: Choosing a new geoid as GMSL changes

## Slide 35: High resolution products
All will be 1 x 1 arcminute grids
All will cover three finite regions of the globe
All will have a static and dynamic component
  Dynamic surface gravity not expected to be ready by 2022
GEOID2022
  Official converter of *TRF2022 ellipsoid heights into NAPGD2022 orthometric heights
DEFLEC2022
  Surface deflections of the vertical in N/S and E/W
GRAV2022
  Surface acceleration of gravity

## Slide 36: The three gridded regions
“North American region”
¼ of the Earth
“Guam/CNMI region”
“American Samoa region”

## Slide 37: Let’s change gears one more time…

## Slide 38: The new Geodetic Toolkit with NADCON 5.0
https://beta.ngs.noaa.gov/gtkweb/

## Slide 39
X, Y, Z
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83
Notes:

## Slide 40
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 41: So much more…
OPUS-Projects being expanded to replace Bluebooking
  Leveling, RTK, Gravity
An entire new database being built
All historic GPS data back to 1997 being reprocessed into the TRFs
A new leveling manual to work in a GPS/geoid “vertical datum”

## Slide 42: So much more…
VERTCON 3 under construction
More GIS friendly products, services and tools being built
Replacement for NGS 58 (“GPS derived ellipsoid heights”) manual nearly complete

## Slide 43: Thank you!

## Slide 44: Questions?

## Slide 45: Extra Slides

## Slide 46: Plate-(pseudo)fixed frames
NAD 83(NSRS2007)
Epoch 2002.0
NAD 83(2011)
Epoch 2010.0
If NAD 83 were truly “plate
fixed” then an 8 year
epoch change would not
yield the systematic
plate rotation seen here.
(*)TRF2022 will determine
a new Euler Pole rotation
for each of 4 plates.
(*)=NA, C, T or P
NAD 83(2011) minus NAD 83(NSRS2007)

## Slide 47: NAD 83’s non-geocentricity
~2.2 m
NAD 83 origin
IGSxx origin
Earth’s Surface
hNAD83
hIGSxx
fNAD83 – fIGSxx
lNAD83 – lIGSxx
hNAD83 – hIGSxx
all vary
smoothly by latitude
and longitude
same
GRS-80
ellipsoid

## Slide 48: Fixed-Epoch Transformation NAD 83 to “2022”

## Slide 49: PRMI (Puerto Rico)

## Slide 50: PRMI (Puerto Rico)

## Slide 51: PRMI (Puerto Rico)

## Slide 52: PRMI (Puerto Rico)

## Slide 53: BRW1 (N. Alaska)

## Slide 54: BRW1 (N. Alaska)

## Slide 55: BRW1 (N. Alaska)

## Slide 56: BRW1 (N. Alaska)

## Slide 57: KOD6 (S. Alaska)

## Slide 58: KOD6 (S. Alaska)

## Slide 59: KOD6 (S. Alaska)

## Slide 60: KOD6 (S. Alaska)

## Slide 61: KOK5 (Hawaii)

## Slide 62: KOK5 (Hawaii)

## Slide 63: KOK5 (Hawaii)

## Slide 64: KOK5 (Hawaii)

## Slide 65: ASPA (Am. Samoa)

## Slide 66: ASPA (Am. Samoa)

## Slide 67: ASPA (Am. Samoa)

## Slide 68: ASPA (Am. Samoa)

## Slide 69: ASPA (Am. Samoa)

## Slide 70: Mariana rotation
Snay (2003) used only one CORS (“GUAM”) to determine the Mariana rotation
  But 2 sites at a minimum are needed to uniquely determine a plate’s rotation
    “CNMI” (since decommissioned) was forced to equal “GUAM” to solve the problem
    Ill-posed, yet the values behave reasonably for GUAM.
    Less reasonable for newer CORS “CNMR”

## Slide 71: GUAM (Guam)

## Slide 72: GUAM (Guam)

## Slide 73: GUAM (Guam)

## Slide 74: GUAM (Guam)

## Slide 75: GUAM (Guam)

## Slide 76: CNMR (CNMI)

## Slide 77: CNMR (CNMI)

## Slide 78: CNMR (CNMI)

## Slide 79: CNMR (CNMI)

## Slide 80: CNMR (CNMI)

## Slide 81
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.

## Slide 82: Time-Dependencies as a service: NATRF2022 and actual survey epochs
CORS best estimate of dh/dt: -2.2 mm / year
NATRF2022 best estimate of dh/dt: -4.2 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
NAD 83 forcibly combined data spanning many years (using HTDP with no vertical modeling) to compute and find one height at one epoch.
NATRF2022 will compute coordinates at survey epoch to show actual motion.
Even gridding surrounding CORS yields better subsidence rates than you have today.
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 83: Time Dependencies as a service: Intra-plate motions
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748

## Slide 84: So…what is “Geopotential”
Geo: Earth
Potential: Gravity Potential Energy
Geopotential: Gravity Potential Energy Field that surrounds the Earth.

## Slide 85: Surely you remember this page from your high school physics textbook?
For example: Choosing
which “W ” value is “the geoid”
0

## Slide 86: Gravity vs Gravitation
Q: But you said “Gravity” potential energy, yet that textbook said “Gravitational” potential energy…
A: Very observant!
  Gravitation: Masses attracting each other
  Gravity: Gravitation plus Centrifugal
    Gravity is what we actually feel on a rotating planet
Warning: Getting in the weeds…