## Slide 1
The
change
you
shape

## Slide 3
What you need to know to prepare for the 2022 National Spatial Reference System (NSRS) Modernization
13 June 2019
Dr. Dru Smith,
NSRS Modernization Manager
NOAA/National Geodetic Survey

## Slide 4: Outline
BLUF
What I’ll be skipping…
Refresher
Shift and Drift
  Replace NAD 83
  Replace NAVD 88
EPP2022 and IFVM2022
Reference Epoch Coordinates from Time-Dependent Coordinates
So much more…

## Slide 5: Bottom Line, Up Front
If you do geospatial work in the USA…
and you work in the National Spatial Reference System..
every product you’ve ever made…
  every survey…
  every map…
  every lidar point cloud…
  every image…
  every DEM…
  WILL have the wrong coordinates on it in 3 years.
  Let’s talk about what this means, why it is happening, and how it will affect things going forward

## Slide 6: What I’ll be skipping…
This topic usually takes 2 hours to cover
Not included today:
  What is…
    NGS and its mission
    The NSRS
    Bluebooking
    GRAV-D
    ITRF
  Why we are modernizing in 2022
All of these topics have been covered extensively in multiple forums in the last few years

## Slide 7: Refresher

## Slide 8: “Modernizing the NSRS” means…
Replacing NAD 83
Replacing NAVD 88
Re-inventing Bluebooking
Improving the Geodetic Toolkit
Better Surveying Methodologies
Blueprint for 2022, Part 3
Blueprint for 2022, Part 1
Blueprint for 2022, Part 2
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 9
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
Sep 2017
NOAA TR NOS NGS 62
32 pages
Geopotential:
Nov 2017
NOAA TR NOS NGS 64
41 pages
Working in the modernized NSRS:
April 2019
NOAA TR NOS NGS 67
77 pages

## Slide 10: Replacing NAD 83
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 11: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  Will include:
  GEOID2022
  DEFLEC2022
  GRAV2022
  DEM2022
  More
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 12: The preeminence of ITRF
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
Rotation of the
North American Plate
Rotation of the
Caribbean Plate
Rotation of the
Pacific Plate
Rotation of the
Mariana Plate
ITRF2014
EPP2022
EPP for “Euler Pole Parameters”
(a way of describing a plate’s rotation)

## Slide 13: Shift and Drift

## Slide 14: Shift
One of the two major changes you’ll see in 2022 is a shift in coordinates
  Latitude, Longitude, Ellipsoid Height: -2 to +4 meters
    Non-geocentricity of NAD 83
  Orthometric Height: -0.5 to +2.0 meters
    Bias and tilt in NAVD 88
  Other shifts will occur in non-CONUS, non-Alaska regions of the USA
  There will be outliers!
    “Old” unsurveyed points might be off by meters if they’ve moved!

## Slide 15: NAD 83(2011) epoch 2010.0 to NATRF2022 epoch 2020.00 (estimate)

## Slide 16: NAVD 88 to NAPGD2022 epoch 2020.00 (estimate)

## Slide 17: Drift
The second major change you’ll see in 2022 is a drift in coordinates
  Everything in the world moves
  Coordinates will be associated with the actual date when the data was taken!

## Slide 18: The wrong question, circa 2022:
“What is the latitude of that point?”
The right question, circa 2022:
“What is the latitude of that point, on some specific date?”

## Slide 19: Drift
The second major change you’ll see in 2022 is a drift in coordinates
  Everything in the world moves
  Coordinates will be associated with the actual date when the data was taken!
  Velocities at all marks can be estimated
    Using a new tool, called the Intra-Frame Velocity Model (IFVM2022)
  Two things will mitigate the pain of time-dependent coordinates:
    “Plate Fixed” frames
    “Reference Epoch” coordinates

## Slide 20: CORS Velocities – ITRF2014

## Slide 21: CORS Velocities – NATRF2022

## Slide 22: EPP2022 and IFVM2022: The two tools that make time dependent geodetic control useable

## Slide 23: There’s really two drifts
The plate rotation is simple (3 parameters per plate)
  Captured in EPP2022
  Horizontal (latitude/longitude) only
  Changes the frame
    ITRF2014 to NATRF2022, PATRF2022, CATRF2022 & MATRF2022
  Doesn’t change the epoch
The residual motions (after removing plate rotation) are complex
  Captured in IFVM2022
  Residual horizontal motion
  All vertical motion
  Changes the epoch
  Doesn’t change the frame
    IFVM = “Intra-frame” velocity model

## Slide 24: Example
It’s 2039 and you are working in San Diego using NATRF2022
You need to compare your work against a competitor’s survey
  Done in 2028, using PATRF2022
NATRF2022
ep. 2028.048
PATRF2022
ep. 2028.048
ITRF2014
ep. 2028.048
NATRF2022
ep. 2039.704
ITRF2014
ep. 2039.704
PATRF2022
ep. 2039.704
EPP2022
EPP2022
EPP2022
EPP2022
IFVM2022
IFVM2022

## Slide 25: Reference Epochs
It seems highly unlikely that surveyors will embrace coordinates with such diversity of epochs
To mitigate that, NGS will issue “snapshots” of the NSRS every five years (called “Reference Epochs”)
  Estimates of coordinates at specific 5 year intervals, based on historic time-dependent coordinates and IFVM2022
Beginning with 2020.00
  Each “snapshot” will be published 2-3 years after the reference epoch
    Thus the 2020.00 Reference Epoch Coordinates get published by the end of calendar year 2022

## Slide 26: Reference Epoch Coordinates from Time-Dependent Coordinates

## Slide 27
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
Assume “h” was determined four different times:
1990: 2.100
1994: 2.110
2002: 2.190
2009: 2.180
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30

## Slide 28
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
All measurements have error. Shown here are the same
values of “h”, but with their error estimates.
1990: 2.100 +/- 0.0375 (3.75 cm)
1994: 2.110 +/- 0.0250 (2.50 cm)
2002: 2.190 +/- 0.0200 (2.00 cm)
2009: 2.180 +/- 0.0250 (2.50 cm)
In the modernized NSRS these time-dependent
coordinates, estimated at the actual date when
the surveys took place, will be called
“Final Discrete Coordinates”

## Slide 29
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In today’s NSRS, a height is held fixed until
replaced. So plotting the height as seen on a datasheet
over time would look like this:

## Slide 30
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the modernized NSRS we will also have an estimate of
crustal motion from IFVM2022
Combining Final Discrete Coordinates
with IFVM2022 allows
NGS to estimate Reference Epoch Coordinates

## Slide 31
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
The IFVM2022 model will match reference epoch coordinates

## Slide 32
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the absence of new survey data, error estimates will
grow through time.

## Slide 33
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
The (in)ability of current approach to
properly inform users of the height of
this mark can be seen in green below.

## Slide 34: Example (v2)
It’s 2039 and you are working in San Diego using NATRF2022 (epoch 2035.00)
You need to compare your work against a competitor’s survey
  Done in 2028, using PATRF2022 (epoch 2025.00)
NATRF2022
ep. 2025.00
PATRF2022
ep. 2025.00
ITRF2014
ep. 2025.00
NATRF2022
ep. 2035.00
ITRF2014
ep. 2035.00
PATRF2022
ep. 2035.00
EPP2022
EPP2022
EPP2022
EPP2022
IFVM2022
IFVM2022

## Slide 35: So much more…
New version of PAGES
  GPS, Galileo, GLONASS, Beidou, QZSS, etc.
  Target: 15 minute occupations
New version of OPUS
  RTK/RTN: 2019
  Leveling, Classical, Gravity: 2020-2025
  Fully integrated (GPS projects with leveling and gravity? No problem!)
  Ease of submission to NGS for inclusion in the NSRS
New Mark Recovery Tool
  Smart-phone enabled. In beta now! beta.ngs.noaa.gov/cgi-bin/recvy_entry_www.prl
Fully integrated toolkit
  NCAT and VDatum

## Slide 36
Take the
session survey
Please complete your session survey on the HxGN LIVE Mobile App

## Slide 37
Thank you

## Slide 38
Questions?

## Slide 39: Extra Slides

## Slide 40: The “why”

## Slide 41: Drivers of change
The current NSRS has issues:
  Non-geocentricity of ellipsoid
  Outdated geoid as the zero height surface
  Does not account for time change
  Significant dependence upon passive marks
More details available in Appendix A of the proceedings of the 2010 Geospatial Summit:
  https://www.ngs.noaa.gov/library/pdfs/SP_NOS_NGS_10.pdf
Fixing these will cause a “shift”
Fixing this will cause a “drift”

## Slide 42: NAD 83’s non-geocentricity
~2.2 m
NAD 83 origin
ITRF2014 origin
Earth’s Surface
hNAD83
hITRF2014
fNAD83 – fITRF2014
lNAD83 – lITRF2014
hNAD83 – hITRF2014
all vary smoothly by latitude and longitude
same
GRS-80
ellipsoid

## Slide 43
H
Earth’s
Surface
The Geoid*
NAVD 88 H=0 reference level
(AKA “the geoid for NAVD 88”)
H (NAVD 88)
Errors in NAVD 88 : ~50 cm average,
100 cm CONUS tilt,
1-2 meters average in Alaska
Outdated geoid (H=0) in NAVD 88
*Current best
estimate from:
GRACE/GOCE satellites
GRAV-D airborne mission
Notes: This slide shows what NGS now knows about the error in NAVD 88 itself. Using a continental geoid computed from the GRACE satellite, a bias and tilt in NAVD 88 has been computed using GPS derived ellipsoid heights on NAVD 88 bench marks. These are now known errors that exist in all NAVD 88 bench marks. This datum realization error, relative to the geoid, is over and above the errors from marks moving.

## Slide 44: Re-inventing Bluebooking
What? | The Old | The New
GPS campaigns | Bluebooking (PAGES, ADJUST, burden on user) | OPUS
Leveling campaigns | Bluebooking / Tied to passive control | OPUS ; GNSS requirements (time, spacing)
Relative Gravity campaigns | Dead bluebook procedure ; Processed separately; Not stored in IDB | OPUS
Absolute Gravity campaigns | Processed separately; Not stored in IDB | OPUS
Classical survey campaigns | Dead bluebook procedure ; Official policy is we don’t take them; Processed separately; Not stored in IDB | OPUS ; GNSS requirements (time, spacing)
GPS campaigns (redux) | OPUS-Projects w/o any way to submit to NGS | OPUS
Single GNSS occupations | OPUS-S or OPUS-RS w/o any way to submit to NGS | OPUS
Mark Recovery | Mark Recovery Page | OPUS ; Browser-based on a smart phone with GPS/Camera/Internet
CORS coordinate functions | Piecewise linear ; years long “repros” ; rare checks on persistent disagreements between daily positions and coordinate functions | Piecewise non-linear ; daily checks on persistent disagreements between daily positions and coordinate functions
RTN/K | No significant interaction with NSRS | RTN alignment service ; RTK/N vectors allowed in OPUS
Historic GPS data | Stored as vectors; occasionally re-adjusted | Raw data stored; massive re-processing possible
ITRF | An acknowledged, but minor role in NSRS | Dominates the NSRS; all values flow from ITRF2014
Coordinates | Time-independent; Occasional readjustment | Time dependent (primary) ; Adjusted to reference epochs every 5 years (secondary)
Geodynamics | HTDP (almost no vertical ; getting dated) | IFVM (3-D, time dependent, method TBD)
Least Squares Adjustments | ADJUST, NETSTAT, GPSCOM/LLSOLV, CALIBRATE, PAGES, Heart of Gold, INERT1, HOACOS, HAVAGO, others? | One common code library, rigorously derived and documented including parameter estimation and hypothesis testing?
Descriptions | WinDESC ; complicated | Possibly a position and photograph?

## Slide 45: Improve the Toolkit
  The Old:
  “Online Adjustment User Services”
  GEOCON
  GEOCON11
  LVL_DH
  ConvbinConvascii
  ENHANCEMENTS
  Gethvlist
  INTERORB
  TOLADD
  Surface Gravity Prediction in the Conterminous USA
  NAVD 88 Gravity Computations
  HTDP (geodynamics)
  Magnetic Declination
  CORPSCON
  The Old:
  VERTCON
  NADCON
  All Hybrid Geoid Models
  All Gravimetric Geoid Models
  All Hybrid DOV Models
  All Gravimetric DOV Models
  14 parameter transformations in HTDP
  XYZWIN
  UTMS
  USNG
  GGPCGP
  SPC83
  DYNAMIC_HT
  IGLD85
  CALIBRATE
  Translev
  WinDESC
  LOCUS
  LOOP
  MTEN4
  “Tidal and Orthometric Elevations”
  INVERSE
  FORWARD
  INVERS3D
  FORWRD3D
Integrate into
NCAT/VDatum
Integrate into
OPUS
Integrate into NSRS Database
Integrate into one new piece of code
Deprecate
Replace
w/ GRAV2022
Replace w/ IFVM2022
Move to “exo-NGS”
software page
  The New:
  EPP2022
  IFVM2022
  SPCS2022
  GEOID2022
  GRAV2022
  More…

## Slide 46: Everything 2022…
Ellipsoid
W0
EPP2022
CORS coordinate functions in ITRF2014
IFVM2022
GM2022
GEOID2022
DOV2022
GRAV2022
DEM2022
Hdyn(f, l, t)
OPUS Mark Recovery
OPUS for GNSS
OPUS for leveling
OPUS for relative gravity
OPUS for classical
OPUS for absolute gravity
NSRS Database
NGS versions of OPUS to:
  Check submissions
  Cluster and process GNSS by “lune”, and load
  Cluster and process all data for reference epoch coordinates, and load
Definitional Constants
Definitional Data
Process/Submit software for users
Software for NGS
Someplace to put that data…
Data delivery system
…and a way to display it all
“alpha” version planned for 2019

## Slide 47: Terminology
The following terms (and more) are defined meticulously in BP3 in a coordinated effort within NGS and with the IERS:
  Point, Mark, Station, Site, ARP, GRP, Site Marker, CORS, the NOAA CORS Network
    GRP = Geometric Reference Point – the official point on a station to which all coordinates refer
As a direct fallout: NGS will no longer provide CORS coordinates at an ARP, only to a GRP
  An antenna has an ARP.
    A CORS only sometimes has an antenna.
      Therefore a CORS only sometimes has an ARP.
      But it always has a GRP.
        The ARP and GRP are only sometimes coincident in space when the antenna is mounted at a CORS
  The GRP gets a Permanent Identifier (PID)

## Slide 48: Terminology
“CORS” is an acronym
  It is singular (S means “Station”, not “Stations”)
  It will no longer be used to describe the network of all such stations
    That will, for now, be called the NOAA CORS Network, or NCN
      Which has a subset of stations called the NOAA Foundation CORS Network, or NFCN
  Its plural form is CORSs
    No apostrophe, No “es” and no skipping the “s”
    GODE is a CORS
      Not “a CORS site”
        And definitely NOT “a CORS Station”
          That’s like “an ATM machine”
    GODE and 1LSU are CORSs
    GODE and 1LSU belong to the NOAA CORS Network
    TMG2 is a NOAA Foundation CORS
    TMG2 and FLF1 are NOAA Foundation CORSs
    TMG2 and FLF1 belong to the NOAA Foundation CORS Network

## Slide 49: Terminology
“OPUS”
  Online Positioning User Service
  Adopted as the general term for all of our online positioning software
    Rather than “-Projects” , “-S” , etc
    Basically “do it with OPUS” should be applicable to a wide variety of tasks
      Recon, Mark Recovery, GPS, Leveling, Gravity, Classical

## Slide 50: Terminology
“GPS Month”
  A span of four consecutive GPS weeks, where the first GPS week in the GPS month is an integer multiple of 4
  GPS Month 0 = GPS weeks 0, 1, 2 and 3
  GPS Month 1 = GPS weeks 4, 5, 6 and 7
  Etc.

## Slide 51: New Types of Coordinates

## Slide 52: New Types of Coordinates
Reported
  “These are from any source where the coordinate is directly reported to NGS without the data necessary for NGS to replicate the coordinate.”
    Scaled
    From NCAT or Vdatum
      NGS Coordinate Conversion and Transformation Tool (NCAT)
    Hand Held / Smartphone
    Reported directly from an RTK rover without data files

## Slide 53: Reported Coordinates

## Slide 54: New Types of Coordinates
Preliminary
  “These are coordinates at survey epoch that have been computed from OPUS, but not yet quality checked and loaded into the National Spatial Reference System Database (NSRS DB).”
    User-computed values, such as they might get today from either OPUS-S or OPUS-Projects
    “Preliminary” coordinates are the only coordinates a user will get directly from OPUS

## Slide 55: New Types of Coordinates
Reference Epoch
  “These are coordinates which have been estimated by NGS, from time-dependent (final discrete and final running) coordinates, at an Official NSRS Reference Epoch (ONRE)”
    NAD 83(2011) epoch 2010.00 (sort of) would’ve fallen under this category
    These will be computed by NGS every 5 years
      On a schedule 2-3 years past ONRE
        2020.00 coordinates will be computed in CY 2022
        2025.00 coordinates will be computed in CY 2027

## Slide 56: New Types of Coordinates
Final Discrete
  “These are coordinates computed by NGS using submitted data and metadata, checked and adjusted and referenced to one survey epoch.”
    These represent the best estimates NGS has of the time-dependent coordinates at any mark
    Could be a:
      Daily solution on one CORS
      The single adjusted value coming from one or more occupations on a passive mark within 1 GPS Month
*
*
More on that in a moment…

## Slide 57: New Types of Coordinates
Final Running
  “Of all types of coordinates on a mark, these are the only ones which will have a coordinate at any time.”
    At a CORS GRP, they will be the coordinate function
      Which will be generated by a “fit” to regularly computed Final Discrete Coordinates (FDCs) on a TBD basis, perhaps daily, perhaps weekly
    On a passive mark, they will come from a mixture of Final Discrete Coordinates (FDCs) and the Intra-Frame Velocity Model (IFVM2022)
      And possibly the time-dependent geoid, DGEOID2022

## Slide 58: New Way of Operating the NOAA CORS Network (NCN)

## Slide 59: New Way of Operating the NOAA CORS Network (NCN)
Each CORS will get a coordinate function
  Actually three functions, X(t), Y(t), Z(t), in the ITRF2014 frame
  In the strict mathematical definition of “function”
    For any given “t”, there is one and only one X , Y and Z
    We actually do this today, just that the functions are piecewise linear
  We are NOT limiting our “modernized NSRS” discussions of CORS coordinate functions to linear functions only!
    But have made no further decisions yet

## Slide 60: Examples of what non-linear CORS coordinate functions look like

## Slide 61: New Way of Operating the NOAA CORS Network (NCN)
Philosophy:
  The NOAA CORS Network (NCN) will be self-consistent, meaning:
    The impact of a user’s CORS choices within their project will not exceed a small, statistically acceptable value:
      Horizontal < 5 mm, Vertical < 10 mm
  On a daily basis NGS must be able to detect, and react to, persistent disagreement between daily solutions and the current “coordinate function” assigned to any CORS in the NOAA CORS Network (NCN)

## Slide 62: Persistent Disagreement
The point:
  It’s not enough to say “each CORS is good to 1 cm in ellipsoid height”.
    That phrase is vague, lacking what it means to be “good to 1 cm”.
  NGS will define and publish “persistent disagreement”
    Possible component: A persistent non-zero average disagreement
    Possible component: A persistently deviating disagreement
  And NGS will define what happens when a CORS exhibits “persistent disagreement”

## Slide 63: New Way for USERS to Process GNSS Projects

## Slide 64: GNSS: Time Span…
GNSS projects have no time limit.
  (Leveling does. More on that later)
  But they will be processed by NGS in GPS Months
*

## Slide 65: GNSS: Processing by users in OPUS
GNSS projects, processed by users using OPUS, must always be processed by GPS month as a first step
  Multiple occupations on a point within a GPS month will be adjusted together
  Coordinate functions from the IGS network or the NOAA CORS Network are the only allowable control
  These are effectively the identical steps NGS will use in-house to compute Final Discrete Coordinates (FDCs) from your data
    Except NGS will merge your data with all other data in the nation during each GPS month
  This process will be built into OPUS as the default, making it easy for users to quickly perform the adjustment
  Afterwards, users may move on to a second step…
*

## Slide 66: GNSS: Processing by users in OPUS
As a second step, a user may do many alternative things…
  Adjust to some epoch that is convenient to them…
  Hold any CORSs or passive control as constraints…
This two-step approach is a form of sequential adjustments and allows a win-win:
  NGS gets to see the user-computed time-dependent “preliminary” coordinates, which have been computed by GPS Month
    Which will be checked against “final discrete” coordinates computed by NGS
  The user gets whatever adjustment and/or coordinates fulfill their contractual needs
  Redundancy checks can occur both within a GPS month (at step 1, if multiple occupations occur in 1 GPS month) and across GPS months (at step 2, if occupations occur in different GPS months)

## Slide 67: New Way of Processing Leveling Projects

## Slide 68: Leveling: Time Span…
Leveling projects must not exceed 12 sequential months
  Longer projects must be broken into sub-projects each spanning less than 12 sequential months
A compromise between:
  Treating “1 GPS Month” as “simultaneous” in the GNSS arena, and
  Acknowledging that leveling surveys often take weeks to months to conduct
Mixed with the reality that:
  You can’t solve for time-dependent orthometric heights in most leveling projects

## Slide 69: Leveling: GNSS required
For the immediate years following 2022, NGS will require that all leveling projects turned in have GNSS on primary control
  Minimum of 3 points
  Maximum spacing of 30 km
  At least two occupations:
    +/- 14 days of beginning of leveling
      But also within the same GPS month
    +/- 14 days of ending leveling
      But also within the same GPS month
  If leveling exceeds 6 months, must have a 3rd, middle occupation
A GNSS “occupation” can mean “RTK/N”!

## Slide 70: Leveling: Step 1 Identify project marks

## Slide 71: Leveling: Step 2 Identify primary control marks (PCM)
Each PCM is within 30 km of at least one other PCM
< 30 km
< 30 km
< 30 km
< 30 km

## Slide 72: Leveling: Step 2 Identify primary control marks (PCM)
No point over 30 km from a PCM

## Slide 73: Leveling: Step 3 Initial GNSS on all PCMs
All PCMs, required: within +/- 2 weeks of the start of leveling
Each PCM, required: 2+ occupations within the same GPS month
All PCMs, recommended: Use the same GPS month

## Slide 74: Leveling: Step 4 Leveling
Finished in under 12 months
If greater than 6 months, need a mid-project GNSS set on PCMs

## Slide 75: Leveling: Step 5 (if 6-12 months) Mid-project GNSS on all PCMs
All PCMs, recommended: Near midpoint of project
Each PCM, required: 2+ occupations within the same GPS month
All PCMs, recommended: Use the same GPS month

## Slide 76: Leveling: Step 6 Final GNSS on all PCMs
All PCMs, required: within +/- 2 weeks of the end of leveling
Each PCM, required: 2+ occupations within the same GPS month
All PCMs, recommended: Use the same GPS month

## Slide 77: Leveling: Processing
All GNSS data processed into GPS months, as per normal processing
These are then adjusted to a mean epoch of the entire leveling survey to yield “representative” orthometric heights that serve as control over the entire leveling project
Stochastic but no time dependency

## Slide 78: Leveling: Processing
The pre-computed GNSS-based orthometric heights are held as stochastic constraints in the adjustment of leveling data
Use math model from NOAA TM NOS NGS 74
Separates out errors in GNSS from Leveling:
  Absolute heights will have standard deviations that are “at GNSS accuracy levels”
  Differential heights will have standard deviations that are “at leveling accuracy levels”

## Slide 79: Leveling: Absolute errors
Consider this quote from a concerned user:
  “In the old NSRS, I could pull the datasheet for a point in California and see that NGS trusted the NAVD 88 height to 1 millimeter. Now, you’re telling me to use RTN to establish orthometric heights in the same area, and I’m getting heights with 4 cm standard deviations! Why are your heights less accurate today than in the past?”

## Slide 80: New Way for NGS to Process and store GNSS Data: Final Discrete Coordinates (FDCs)

## Slide 81: GNSS: Monthly workflow…
Every GPS month (say the first Monday of that GPS month), NGS will “process the GPS month of 12-16 weeks ago” by doing the following:
  Ensure that the “final” IGS orbits for the GPS month that spans 12-16 weeks prior are available
    If not, hold off on this until they are
  Create an in-house project named for that prior GPS month
  Farm all data (collected during that GPS month) from all projects submitted to NGS, and put them all into the in-house project

## Slide 82: Processing by GPS Month…
GPS Month 587
GPS Month 588
GPS Month 589
GPS Month 590
GPS Month 591
GPS Month 592
GPS Month 593
GPS Month 594
All GNSS data collected in this
GPS month…
…are processed in this GPS month…
…to create Final Discrete coordinates for
this GPS month….
…which are loaded into the
NSRS database in this GPS month.

## Slide 83: Processing by GPS Month…
GPS Month 587
GPS Month 588
GPS Month 589
GPS Month 590
GPS Month 591
GPS Month 592
GPS Month 593
GPS Month 594
All GNSS data collected in this
GPS month…
…are processed in this GPS month…
…to create Final Discrete coordinates for
this GPS month….
…which are loaded into the
NSRS database in this GPS month.

## Slide 84: GNSS: Monthly workflow…
Adjust all that data together
Take the results of this adjustment and load them into the NSRS database as “final discrete” coordinates

## Slide 85: GNSS: Monthly workflow…
Q: What about users’ projects that span more than 12-16 weeks?
A: NGS will provide a way for a user to “allow NGS to farm my data as it is loaded to my ongoing project”
  Thus NGS needn’t wait for them to finish their project and click “submit”.
  Will require some sort of metadata validity statement from the user for each data file uploaded

## Slide 86: GNSS: Monthly workflow…
Q: What if a user turns in data more than 12-16 weeks after it was collected?
A: NGS will have a “holding bin” for such data. Occasionally, but not more than 1/year, NGS will sweep up all data in the holding bin, and put that data into the proper in-house GPS-month-based projects, depending on the GPS month of that data.
  Since those in-house projects have already been adjusted once before using data that WAS submitted within the 12-16 week limit, and “final discrete” coordinates were computed on those early-submitted data, NGS will hold the “final discrete” coordinates on that early-submitted data as “fixed”, and adjust the later-submitted data only.

## Slide 87: New Way for NGS to Process and store GNSS Data: Reference Epoch Coordinates (RECs)

## Slide 88: GNSS: Every five years…
Official NSRS Reference Epochs (ONREs) will happen every five years, beginning with 2020.00.
Every ONRE will have a project associated with it
  To estimate the Reference Epoch Coordinates (RECs) at each ONRE
  That project will begin 2 years after the ONRE and will end 3 years after it
    Thus the project to create 2020.00 RECs will run January 1-December 31, 2022
    Using data collected through the end of 2021
Error estimates in RECs will grow larger every five years for those points which are not regularly observed
Once computed, the REC at an ONRE for a point will stand forever, unless corrected for a blunder

## Slide 89
Time “t ” when
all four TRFs and
ITRF2014 are identical.
(2020.0)
0
MATRF2022
MATRF2022
Rotation of Mariana Plate
t=t + Dt
(“the future”)
0
t=t - Dt
(“the past”)
0
CATRF2022
CATRF2022
NATRF2022
PATRF2022
NATRF2022
PATRF2022
Rotation of Caribbean Plate
ITRF2014 frame through time
ITRF2014 frame
ITRF2014 frame
Rotation of Pacific Plate
Rotation of North American Plate
The relation of five global reference
frames through time.
Rotations are not to scale

## Slide 90: These are part of the NSRS
Hor Datums / Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations / Conversions
USSD | NGVD 29 | IGLD55 | GEOID90 | NADCON
NAD 27 | NAVD 88 | IGLD85 | GEOID93 | VERTCON
NAD 83 | PRVD02 |  | ALASKA94 | 
 | ASVD02 |  | GEOID96 | SPCS 27
 | NMVD03 |  | GEOID99 | SPCS 83
 | GUVD04 |  | GEOID03 | 
 | VIVD09 |  | GEOID06 | 
 |  |  | GEOID09 | 
 |  |  | GEOID12(A,B) | 
These are select entries, not a complete list

## Slide 91: These are not part of the NSRS
Hor Datums / Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations / Conversions
WGS 84 | IHRS |  | OSU91A | CORPSCON
ITRF |  |  | EGM96 | Appendix B.6 of DMA TR 8350.2 (WGS 84)
IGS |  |  | EGM2008 | Oregon Coordinate Reference System
 |  |  |  | The Kansas Regional Coordinate System
These are select entries, not a complete list

## Slide 92: Mixing NSRS and non-NSRS?
Just do it right
Right:
  The Oregon CRS has a mathematically defined relationship to the NSRS
Wrong:
  “WGS 84 is the same as NAD 83”
  “WGS 84 is the same as the ITRF”
  “Sub-meter accuracy is possible using WGS 84”
    Such statements gloss over critical facts about history, accuracy and application

## Slide 93: Accuracy
Consider your users’ accuracy needs
  3 Meters?
    Then WGS 84 is NAD 83
    Global 14 parameter transformations will suffice
  3 Decimeters?
    Then NAD 83(2011) is NAD 83(NSRS2007)
      But NAD 83(1986) is not the same as NAD 83(HARN)
    NADCON will suffice as a transformation
  3 Centimeters?
    Every detail matters

## Slide 94
Watch the grid!
Time Changes - Horizontal

## Slide 95: Time-Dependency
The IGS14 frame is not beholden to any tectonic plate
  Thus the four plates with U.S. populations will have time-dependent latitudes/longitudes:
    North America: 1-3 cm / year (CONUS, Alaska)
    Pacific: 7-8 cm / year (Hawaii, AS)
    Caribbean: 1-2 cm / year (PR, USVI)
    Mariana: 1-4 cm / year (Guam, CNMI)

## Slide 96
What does it mean to provide time-dependent coordinates in 5 frames?

## Slide 97: BSMK (North Dakota)

## Slide 98: BSMK (North Dakota)
NATRF2022 Latitude is CONSTANT over time
As per NGS policy decision circa 2018:
t0 = 2020.0

## Slide 99: BSMK (North Dakota)
NATRF2022 Longitude is constant over time

## Slide 100: BSMK (North Dakota)
No matter WHAT frame, the ellipsoid height is dropping over time

## Slide 101: PIN1 (S. California)

## Slide 102: PIN1 (S. California)
Latitude in NATRF2022 and PATRF2022 change over time

## Slide 103: PIN1 (S. California)
Longitude in NATRF2022 and PATRF2022 change over time

## Slide 104: PIN1 (S. California)
No matter WHAT frame, the ellipsoid height is rising over time

## Slide 105: Definitional Relationship
Time-dependent ellipsoid heights
come from time-dependent
CORS coordinates which serve as control for your time-dependent GNSS survey.
They will be modeled in the IFVM
Time-dependent geoid undulations
are modeled in the dynamic component of GEOID2022 (“DGEOID2022”), which will come from the geoid monitoring service, or GeMS.

## Slide 106
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022