## Slide 1
The modernized NSRS
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
Some answers up front
Why “2022”?
Brief overview
  New Reference Frames / Datum
  Expected Changes
Recent progress
Re-prioritization: a “data first” approach
Timeline

## Slide 3: Answers …
What is changing?
  All horizontal datums and vertical datums in the NSRS
    NAD 83 , NAVD 88 , etc.
  Thus every coordinate for everything in the USA is going to change by decimeters to meters
Why?
  Predominantly to keep up with technology.
    Global proliferation of real time cm-accuracy positioning (in the hands of people who have no understanding of geodesy, datums, plate tectonics, error sources or other subtleties) is rapidly approaching.
      Many surveying, mapping and navigation professionals already enjoy this accuracy.
    The current datums have systematic errors exceeding 1 meter.
When is it changing?
  Mid 2025
Will it be an immediate or gradual change?
  Immediate

## Slide 4: Modernized NSRS and “2022”
Intent: release the modernized NSRS in 2022
Years ago, many yet-to-be-built components were given “2022” in their names:
  GEOID2022, NATRF2022, NAPGD2022, etc.
“We are delayed” – announcement in June 2020
To avoid confusion with long-standing communications, NGS chose to leave “2022” in the names
When will we be done? Mid-2025

## Slide 5: Federal Users of the NSRS
Notes: Many of these users also sit on the Federal Geodetic Control Subcommittee, so there is a feedback loop between the providers of geodetic control (NGS) and the users of that control.

## Slide 6: Brief overview: Four New Reference Frames and One New Geopotential Datum

## Slide 7: Replacing NAD 83
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 8: NAD 83(2011) epoch 2010.0 to NATRF2022 epoch 2020.00 (estimate)

## Slide 9: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  Will include:
  GEOID2022
  DEFLEC2022
  GRAV2022
  DEM2022
  More
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
A HUGE component of this
effort is GRAV-D:
Gravity for the Redefinition of
the American Vertical Datum

## Slide 10: Expected changes to orthometric heights

## Slide 11: Re-prioritization: a “data first” approach

## Slide 12: Re-prioritization
NGS has recently decided to release all of the modernized NSRS data before we have fully completed all support tools
If we do not take this approach, we are not likely to see the modernized NSRS defined and released until 2030

## Slide 13: Data
Upon release, the modernized NSRS will consist of this data:
  The NOAA CORS Network (NCN) operating on ITRF2020
  NATRF2022, PATRF2022, MATRF2022, CATRF2022 defined relative to ITRF2020
  NAPGD2022, including:
    GM2022, GEOID2022, DEFLEC2022, GRAV2022
  Geometric (XYZ / flh) and orthometric (H) reference epoch coordinates (RECs) at 2020.00 at those passive control with the observations to support such coordinates
  Geometric (XYZ / flh) and orthometric (H) survey epoch coordinates (SECs) at survey epochs between about 1994 and 2020 at those passive control with the observations to support such coordinates
  State Plane Coordinates of 2022 (SPCS2022), plus UTM and USNG
  NADCON
    Connecting NAD 83(2011/MA11/PA11) epoch 2010.00 to N/P/M/CATRF2022 epoch 2020.00
  VERTCON
    Connecting NAVD 88, PRVD02, ASVD02, NMVD03, GUVD04 and VIVD09 to NAPGD2022 epoch 2020.00

## Slide 14: Tools
At a minimum, NGS is targeting these tools upon release:
  A Data Delivery System capable of yielding:
    Coordinates on survey marks
    Information on Continuously Operating GNSS Reference Stations
  A downloadable version of LASER
  NCAT and Vdatum capable of invoking NADCON, VERTCON and SPCS2022
  A few more…

## Slide 15: Timeline

## Slide 16: Timeline
Resources are being diverted from tool building to the assurance of quality data first and foremost
As such, based on this new approach, NGS anticipates the release of all data, and limited tools, by the middle of 2025.
Work on additional tools will continue in the out-years

## Slide 17: Thank you!

## Slide 18: Questions?