## Slide 1
State Plane 2022
A Tale of Change, Collaboration,
and Redemption
Michael Dennis, RLS, PE
Geodesist
michael.dennis@noaa.gov
2018 AGIC Education and Training Symposium
Prescott, Arizona
September 19-21, 2018

## Slide 2
geodesy.noaa.gov

## Slide 3
It’s easy! Just click this button!
Projected Coordinates
Projected Coordinates
Latitude
Longitude
Northing (y)
Easting (x)

## Slide 4
Questions?
The End
APPLAUSE

## Slide 5: A New State Plane Coordinate System
State Plane Coordinate System of 2022 (SPCS2022)
  Referenced to 2022 Terrestrial Reference Frames (TRFs)
  Based on same reference ellipsoid as SPCS 83 (GRS 80)
  Same 3 conformal projection types as SPCS 83 and 27:
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 6: About SPCS2022…
State Plane will change in the 2022
NGS will collaborate with stakeholders
  Input on SPCS2022 policy and procedures (DONE!)
  Can submit requests and proposals for their state
As for redemption…
  Make SPCS2022 more useful than previous SPCS
  Will try to accommodate what stakeholders want
  May require compromise and soul-searching, to save both NGS and stakeholders from error…

## Slide 7: The Plan
Background
  Recent NGS activity on SPCS2022
  A bit of SPCS history
Overview of draft SPCS2022 policy & procedures
  Cover main characteristics
  Explain concepts, give examples
Responses to the SPCS2022 Federal Register Notice
  Summarize nationwide input
  The Arizona response
See SPCS2022 poster on display!

## Slide 8
geodesy.noaa.gov/SPCS/

## Slide 9: Who attended the SPCS2022 webinars?
Location | Mar 8 | Apr 12 | Location | Mar 8 | Apr 12 | Location | Mar 8 | Apr 12
Alabama | 7 | 8 | Maryland | 25 | 20 | Rhode Island | 0 | 1
Alaska | 26 | 20 | Massachusetts | 1 | 1 | South Carolina | 7 | 6
Arizona | 48 | 42 | Michigan | 34 | 57 | South Dakota | 7 | 4
Arkansas | 1 | 1 | Minnesota | 124 | 34 | Tennessee | 1 | 1
California | 35 | 30 | Mississippi | 8 | 6 | Texas | 20 | 16
Colorado | 17 | 25 | Missouri | 7 | 11 | Utah | 2 | 9
Connecticut | 4 | 11 | Montana | 16 | 13 | Vermont | 0 | 3
Delaware | 1 | 2 | Nebraska | 16 | 11 | Virginia | 8 | 5
Florida | 52 | 44 | Nevada | 5 | 1 | Washington | 12 | 16
Georgia | 8 | 3 | New Hampshire | 1 | 1 | West Virginia | 1 | 0
Hawaii | 5 | 6 | New Jersey | 4 | 1 | Wisconsin | 9 | 27
Idaho | 12 | 11 | New Mexico | 12 | 7 | Wyoming | 3 | 2
Illinois | 15 | 12 | New York | 4 | 5 | American Samoa | 0 | 0
Indiana | 4 | 7 | North Carolina | 10 | 8 | District of Columbia | 2 | 1
Iowa | 6 | 7 | North Dakota | 33 | 13 | Guam | 0 | 0
Kansas | 5 | 3 | Ohio | 31 | 24 | Mariana Islands | 0 | 0
Kentucky | 5 | 5 | Oklahoma | 3 | 1 | Puerto Rico | 2 | 3
Louisiana | 13 | 10 | Oregon | 53 | 23 | US Virgin Islands | 0 | 1
Maine | 1 | 1 | Pennsylvania | 23 | 18 | International | 8 | 13

## Slide 10: Federal Register Notice
https://www.federalregister.gov/
Announced draft SPCS2022 Policy and Procedures
Also asked for input on “special purpose” zones
Public comment period ended Aug 31, 2018

## Slide 11: History and Future of State Plane
SPCS created 85 years ago
  SPCS 27: 1933 – 1986 (53 years, with some changes)
  SPCS 83: 1986 – 2022 (36 years, with some changes)
  SPCS2022: 2022 – ? (at least a few decades…)
SPCS2022 will likely be around for a long time
  Honor the history and legacy of SPCS…
  …while building a system for the future

## Slide 12
State Plane Coordinate Systems of 1927 (134 zones) and 1983 (125 zones)
Guam SPCS 27 zone a non-conformal projection
American Samoa only in SPCS 27, not SPCS 83
Two zones in SPCS 27, one in SPCS 83
Guam SPCS 83 zone added in 1995

## Slide 13
Final SPCS 27, as of 1968 (112 zones in CONUS, 131 zones total)
Reduced distortion zones added: CA 7 (1945) MI (1964)

## Slide 14
Final SPCS 83, as of 2001 (108 zones in CONUS, 125 zones total)
KY statewide zone added in 2001

## Slide 15
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 16: Linear distortion at topo surface
Policy§II.C and Procedures§5.c.
Distortion for design evaluated at topo surface
  Minimize range and mean distortion in zone
  Account for cities with distortion weighted by population
Design not evaluated at the ellipsoid surface
  Nobody lives or works on the ellipsoid
  Likely used in past because it is easier
Projection scaled to topo surface (“ground”)
  Reduces difference between “grid” and “ground”
  Topographic ellipsoid height not part of definition

## Slide 17
Grid distance > ellipsoid distance
Projection axis
Linear distortion with respect to ellipsoid
Ellipsoid surface
Grid distance < ellipsoid distance
Ellipsoid distance
Ellipsoid distance
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)

## Slide 18
Grid distance < ellipsoid distance < ground distance
Grid distance > ellipsoid distance < ground distance
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
Projection axis

## Slide 19
Projection surface (non-intersecting)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
Grid distance > ellipsoid distance ≈ ground distance
This design approach will be used for SPCS2022 (minimizes distortion with respect to topography)
Projection axis

## Slide 20: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Nominal distortion criterion (on ellipsoid) for SPCS 27 and 83 zones (although greatly exceeded for some zones in SPCS 83).

## Slide 21: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion range (at ground) for zones designed by NGS, as proposed in draft SPCS2022 policy and procedures.

## Slide 22: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion criterion (at ground) often used for “low distortion projection” (LDPs); designed by others for SPCS2022 (not by NGS)

## Slide 23
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 24
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 25: Default SPCS2022 designs
Policy§IV and Procedures§5.g.
For complete system even with no stakeholder input
  To ensure coverage of all states and U.S. territories
Nearly same as SPCS 83 but with some modifications
  Almost all zone projection types and extents the same
  Modified to align with SPCS2022 policy and procedures
  Small number of zones may change projection type, extents
Modifications to align with SPCS2022 policy:
  Scale redefined with respect to topographic surface
  One-parallel Lambert and local Oblique Mercator

## Slide 26: Examples of combined characteristics
Characteristics for default design examples:
  Designs are “SPCS 83-like”
  But minimize linear distortion at “ground”
    Minimize distortion range and mean for entire zone
    Also mean distortion of cities (weighted by population)
  Define LCC projections with 1 standard parallel
Example default zones:
  Arizona Central Zone (Transverse Mercator)
  Colorado South Zone (Lambert Conformal Conic)

## Slide 27
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
Ellipsoid surface
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface

## Slide 28
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
Ellipsoid surface
Topographic surface

## Slide 29
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
Only way to reduce variation in distortion is to change projection axis location.
IMPORTANT: For large areas, there is no single defining ellipsoid height, h, for scaling the projection.
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface

## Slide 34: Default SPCS2022 would look a lot like SPCS 83…

## Slide 35: What changes for default designs?
Most zones will keep same extents and projection type
Possible changes in projection types and zone extents
  1 or 2 OM zones for FL peninsula (currently 2 TM zones)
  1 OM zone for Hawaii (replaces 5 TM zones)
  Include Guam and CNMI in 1 TM zone (currently only Guam)
  Define LCC zone for American Samoa (no SPCS 83 zone)
  Redefine AK zones to better correspond to land use
  Add zone for Washington D.C.
Examples follow of zones where proposed projection type and/or extents change.

## Slide 40
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 41: Statewide and “layered” zones
Policy§III.A.2.
Limitations
  Max of TWO layers: Statewide and sub-zones
  If two layers, one MUST be statewide
  Minimum subzone dimension > 50 km
States often want statewide and small zones
  Statewide: Single geometry required for state GIS
  Sub-zones: Lower distortion for surveying/engineering
Accommodates state needs, but with restrictions
  Prevent poor design choices for statewide zones
One already exists in SPCS 83…

## Slide 42: Kentucky layered zones
 |  | North | South | 
N parallel |  | 38°58’N | 37°56’N | 
S parallel |  | 37°58’N | 36°44’N | 
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | 
Max |  | +17 | +42 | 
Mean |  | -56 | -67 | 
“Layered” zones
SPCS 83 Kentucky N and S zones (Lambert Conformal Conic)

## Slide 43: Kentucky layered zones
 |  | North | South | Statewide
N parallel |  | 38°58’N | 37°56’N | 38°40’N
S parallel |  | 37°58’N | 36°44’N | 37°05’N
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | -166
Max |  | +17 | +42 | +181
Mean |  | -56 | -67 | -58
“Layered” zones
SPCS 83 Kentucky statewide zone (Lambert Conformal Conic)

## Slide 46
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 47: Linear distortion design criteria
Procedures §4.b.i-ii and§5.c.i.
NGS design of zones requested by stakeholders
  Limited to zones with 50-400 ppm distortion criterion
    50 ppm = 5 cm/km = 0.3 ft/mi = 1:20,000
    400 ppm = 40 cm/km = 2.1 ft/mi = 1:2,500
Design criterion < 50 ppm (i.e., “low distortion”)
  Low distortion projections (LDPs)
  Must be designed by others (not by NGS)
  Proposed and final design reviewed by NGS

## Slide 48: Minimum LDP distortion & zone size
Procedures§5.c.ii
Create largest zone that meets distortion criterion
  To avoid creating excessive number very small zones
Minimum distortion design criterion
  20 ppm = 2 cm/km = 0.1 ft/mi = 1:50,000
  Nominal zone width of 114 km (71 miles)
  Nominal height change of 255 m (836 ft)
Minimum allowable zone width 50 km (31 miles)
  Exception: if height change in zone > 250 m (820 ft)
  Note: 50 km corresponds to approx ±5 ppm distortion

## Slide 49
±100 ppm (±0.5 ft/mile)
255 km (158 miles)
Zone widths for distortion due to curvature
Ellipsoid surface
±400 ppm (±2.1 ft/mile)
508 km (316 miles)
Projection surface
Projection surface
Max SPCS2022 distortion; also UTM zone width
Nominal SPCS 83 and 27 zone width

## Slide 50
±20 ppm (±0.1 ft/mile)
114 km (71 miles)
Zone widths for distortion due to curvature
Ellipsoid surface
±50 ppm (±0.3 ft/mile)
180 km (112 miles)
Projection
surface
Minimum distortion criterion for NGS designs
Minimum distortion criterion for LDP designs
NOTE: Change in height of 255 m (836 ft) causes 20 ppm change in distortion
Distortion due to height changes at rates of:
  15.7 ppm per 100 m
  4.8 ppm per 100 ft

## Slide 55
Area of state within:
±10 ppm = 38%
±20 ppm = 60%
±30 ppm = 73%
±40 ppm = 81%
Cities within:
±10 ppm = 77.8%
±20 ppm = 94.0%
±30 ppm = 96.2%
±40 ppm = 98.6%
Population within:
±10 ppm = 96.76%
±20 ppm = 99.79%
±30 ppm = 99.85%
±40 ppm = 99.87%

## Slide 56: Maricopa County

## Slide 58
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 59: “Special purpose” zones
In Federal Register Notice (not in policy & procedures)
For areas with inadequate SPCS zone coverage
  Usually areas that are in more than one zone
Categories:
  Major urban areas (e.g., New York, Chicago, St. Louis, Denver)
  Large Indian reservations (e.g., Navajo Nation)
  Federal applications covering large areas (e.g., coastal mapping of Atlantic Coast; Grand Canyon National Park)
Permitted for metro areas in 1977 policy (but never used)
Only in FRN, not in draft policy & procedures

## Slide 60: Navajo Nation

## Slide 63
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 64: Linear units
Policy§II.D and E
All linear parameters defined in meters
Will also give output in feet version if specified by state
Policy§IV.C (for default zones only)
Will use foot as defined currently for SPCS 83
  Appendix C of NOAA Special Publication NOS NGS 13

## Slide 66
Linear distortion at topographic surface
One-parallel Lambert Conformal Conic projections
Default SPCS2022 zone designs
Statewide and “layered” zones
Linear distortion design criteria
  Maximum and minimum zone size and distortion
  Low distortion projections (LDPs)
“Special purpose” zones (in FRN only)
Linear units
Submittal process and deadlines
  For Federal Register Notice comments
  For requests, proposals, and submittal of designs
Overview: Policy, Procedures, and FRN

## Slide 67: Overview of FRN feedback
FRN public comment period April 18-Aug 31
  For draft SPCS2022 policy & procedures
  Wide variety of formats and content
  Individuals, organizations, and groups of organizations
Received 41 unique responses:
  4 national in scope (3 from USGS)
  3 for Indian tribes
  1 from NGS Rocky Mountain Regional Advisor
  33 from states
105 people represented by name
97 organizations represented

## Slide 68: Organizations represented
1 federal agency (USGS)
10 Indian tribes
23 states (includes state and private organizations)
  17 state DOTs
  12 state GIS/GIO/cartographer offices
  21 state professional societies (surveying and GIS)
  12 universities and colleges
  6 city and county groups
  7 private companies
  10 other state organizations

## Slide 70: The 5 FRN questions
Usage of current SPCS in your organization.
Whether default SPCS2022 definitions impose hardship or are beneficial.
Whether there is sufficient flexibility in SPCS2022 characteristics.
Whether the SPCS2022 deadlines are acceptable.
Whether “special purpose” zones in SPCS2022 would be beneficial, problematic, or irrelevant.

## Slide 71: Responses to the 5 FRN questions

## Slide 72: The Arizona FRN response
From AGIC, APLS, and NAU
Response to FRN questions
  SPCS 83 in statute and used, along with regional LDPs
  Update is opportunity to go beyond default design
  Insufficient flexibility: lack of special purpose zones and no design tools
  Deadlines acceptable if design support provided
  Special purpose zones in SPCS2022 beneficial
    Navajo Nation, Grand Canyon, DOT & utility corridors
    Gives opportunity to explore options for SPCS2022 zones

## Slide 73: Summary of other FRN input

## Slide 74: Deadlines for SPCS2022 requests
SPCS2022 Procedures (draft)
Consensus input per SPCS2022 procedures
  Requests for designs done by NGS
  Proposals for designs by contributing partners
Submittal of approved designs
  Proposal must first be approved by NGS
  Designs must be complete for NGS to review
Later requests will be for changes to SPCS2022
NGS.SPCS@noaa.gov
by December 31, 2019 for requests and proposals
by December 31, 2020 for submittal of approved designs

## Slide 75: Summary
Draft SPCS2022 policy and procedures
  Standardized definitions and computations
  Designed with respect to “ground”
  Default designs similar to existing SPCS 83
  Can include a statewide zone plus one subzone layer
  LDPs can be used but must be designed by others
Federal Register Notice (FRN) input received
  On SPCS2022 policy & procedures
  On “special purpose” zones
Consensus state stakeholder input required for SPCS2022 zone requests, proposals, and designs
P.S. Default and statewide zones design maps available for download at ftp://www.ngs.noaa.gov/pub/SPCS/DistortionMaps/