## Slide 1
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
Alabama Society of Prof. Land Surveyors
2017 Annual Conference
Pelham, Alabama
October 18, 2017
NGS Control Mark Datasheets

## Slide 2
Learn alternate ways to obtain datasheets while in the office, or in the field.
Learn about the different sections of datasheets
Learn about important differences in the information that is found in certain sections of the datasheet.
Goal today: To improve understanding of NGS datasheets

## Slide 3
Where to Find NGS datasheets

## Slide 4
METHODS TO OBTAIN DATASHEETS
“Classical” NGS website retrieval
NGS Data Explorer retrieval
DSWorld software with Google Earth
Smart Phone App - “FindAControl” *
Find-A-Control
(not an NGS product)
CLASSICAL METHOD
DSWorld
NGS DATA EXPLORER

## Slide 5
CLASSICAL Retrieval
Interactive Map Option
You can also find a Project ID using a PID
Useful information

## Slide 6
Interactive map method
Statewide datasheet extractions- latest month is available here
Go To “classical method”
“Text format” datasheet retrievals, or…
“Shapefile format” for GIS functionality

## Slide 7
NGS Data Explorer

## Slide 8
Sample search using NGS “Data Explorer” tool

## Slide 9
Data Explorer Example of Interest

## Slide 10
“CAUTION EXAMPLE”
DJ1389

## Slide 11
DSWorld Retrievals - software developed by Malcolm Archer-Shee
Download this free program from the NGS website at – http://www.ngs.noaa.gov/PC_PROD/PARTNERS/index.shtml
* Search for DSWorld

## Slide 12
DSWorld - Retrievals
Short Demo of DSWorld program (live).

## Slide 13
SMART PHONE or TABLET APP --- Find-A-Control
Android and iOS Application - NOT an NGS product

## Slide 14
DATASHEET SECTIONS:
Basic Metadata
Current Survey Control
Accuracy
Data Determination Methodology
Projections
Azimuth Marks (old hz marks only)
Superseded Survey Control
U.S. National Grid
Monument Information
History
Description and Recoveries
* Information is pulled from tables and
assembled upon retrieval request.

## Slide 15
THE “PID”….. IT IS IMPORTANT
BASIC METADATA SECTION OF EACH DATA SHEET
VERSION # matters to some vendor software programs
dsdata.txt is a guide to understanding datasheet info

## Slide 16
OPUS “SHARE” DATASHEET
CLASSICAL DATASHEET FROM NGS “INTEGRATED DATABASE” (IDB).

## Slide 17
PIDs – IDB vs OPUS Database
DL8801 - PID from NGS IDB
BBBY50 - PID from OPUS Database

## Slide 18
Why is the “PID” important?
The PID is the key to the NGS database which contains more than 1.5 million marks
Twelve stations are named “AIRPORT BEACON” in Alabama
Each one has a unique PERMANENT IDENTIFIER (six character PID)

## Slide 19
Name Search for AL Found
3 - A
3 - ADAMS
12 - AIRPORT BEACON
2 - ALLISON
3 - AP STA A
- ARP
- BM

## Slide 20
THE “PID”….. IT IS IMPORTANT
BASIC METADATA SECTION OF EACH DATA SHEET
VERSION # matters to some vendor software programs
dsdata.txt is a guide to understanding datasheet info

## Slide 21
Three Primary Types of “MODERN” Geodetic Marks:
Leveled only
GPS-Observed only
Leveled and GPS-Observed on same mark
NOTE: there are many old triangulation stations that still exist in the NGS database…. CAUTION: avoid mixing old triangulation data with modern GPS-surveyed marks, unless updated by GNSS observations

## Slide 22
Published “CURRENT SURVEY CONTROL” for a LEVELED-ONLY mark. (NOT GPS observed)
Note Handheld GPS Pos.
Another Vertical Mark Example
Note Position
SCALED from Topo map

## Slide 23
This mark was observed only with GPS (it WAS NOT leveled) -
published height was GPS derived using Geoid model
This mark is also…. GPS-Only

## Slide 24
15 vertical
source options
This mark WAS observed with GPS, and it WAS separately leveled
Sources: ADJUSTED, ADJ_UNCH, POSTED, READJUST, N_HEIGHT, RESET, COMPUTED, GPSCONLV, LEVELING, H_LEVEL, GPS_OBS, VERT_ANG, SCALED, U_HEIGHT, VERTCON
Each type is explained in the “dsdata.txt” document

## Slide 25
“…CONTROL” Section continued
Cartesian
Coordinates
Laplace Correction - combined with astronomic azimuth, yields the geodetic azimuth
Geoid Height -separation between Geoid and the reference ellipsoid (negative in CONUS)
Dynamic Height -geopotential value at the mark (NOT an orthometric height).
Modeled Gravity – interpolated from observed gravity values
Vertical Order Will be 2nd order (or better). NGS does not accept 3rd order, except on “Resets”
* HEIGHTS ARE SEPARATELY DETERMINED, NOT COMPUTED.

## Slide 26
ACCURACY STANDARDS SECTION
(replaces Hz Order & Class for marks)
Clicking on the “here” link generates the following table
Local Accuracies

## Slide 27
THE NEXT SECTION EXPLAINS HOW THE PUBLISHED VALUES WERE DETERMINED

## Slide 28
Leveled
in ~1934
Adjusted
in 1991
(re-adjusted)
Caution: don’t overlook the age of the observations

## Slide 29
PHOTOGRAPH SECTION

## Slide 30
SECTION PROVIDING STATE PLANE and
UTM COORDINATES

## Slide 31
SECTION SHOWING SUPERSEDED VALUES
*
*
*
*

## Slide 32
SECTION PROVIDING THE MARK’S
NATIONAL GRID ADDRESS
U. S. National Grid (USNG) system is a FGDC standard, developed to improve public safety and commerce.
http://www.fgdc.gov/usng

## Slide 33
Mark Description Section - Two examples
(Coast and Geodetic Survey disk)
(set by Barron Co. WI )

## Slide 34
SECTION SHOWING THE MARK’S
“SETTING AND RECOVERY HISTORY”

## Slide 35
STATION RECOVERY NOTES - BE AWARE THAT RECOVERY NOTES CAN SOMETIMES BE MISLEADING!
Mark originally set by NGS (CGS) in 1948
17 YEARS LATER

## Slide 36
SECTION OF THE DATASHEET SHOWING THE STATION DESCRIPTION … (TO-REACH and TIES)
To-Reach Info
Ties

## Slide 37
FINALLY,
WATCH FOR NOTIFICATION THAT YOUR DATASHEET(S) EXTRACTION IS COMPLETE
If you do not see this message at the end, you did not get all of the datasheets that you requested.

## Slide 38
Ever searched for a mark that wasn’t there?
STATION RECOVERY NOTES.

## Slide 39
STATION RECOVERY NOTES
Recovery Note Terms
Good - Mark is in good shape and has no issues to note.
Poor - Mark has issues. Can be disk has scars (mutilated),
overall monument leaning, guardrail place above
mark, etc.
Destroyed - Mark will only be listed as “destroyed” when
evidence is submitted to validate mark is
gone.
- Take pictures as evidence

## Slide 40
? ? QUESTIONS ? ?