## Slide 1: Aspects of the Intra-Frame Velocity (Deformation) Models for the U.S. N.S.R.S
Daniel R. Roman, Ph.D.
Chief Geodesist
NOAA’s National Geodetic Survey

## Slide 2: Outline
Existing National Spatial Reference System
The Need for Change
Starting Point: a Densified-ITRF
The four TRF’s
NAPGD 2022
Surveying post-2022
Summary

## Slide 3: Existing U.S. N.S.R.S.
North American Datum of 1983 (NAD 83)
“Static” Reference Frame
80,000 passive control marks
U.S.: NAD 83 (2011/PA11/MA11)
Canada: NAD83 (CSRS)
Processing performed in ITRF14
HTDP transforms to ITRF96
ITRF 96 => NAD 83 transform. based on 12 global sites
NAD 83 Geocenter from Transit
North American Vertical Datum of 1988 (NAVD 88)
Helmert Orthometric Heights
500,000 passive control marks
Tied at one point in Canada
Adjustment in geopotential numbers
U.S., Canada and Mexico
However, only U.S. adopted
Interpolates static gravity field
Produces consistent heights

## Slide 4: The Need for Change
Issues with NAD 83
~2.24 m
NAD 83 origin
“2022” origin
Earth’s Surface
hNAD83
h”2022”
Simplified concept of NAD 83 vs. “2022”
fNAD83 – f”2022”
lNAD83 – l”2022”
hNAD83 – h”2022”
all vary smoothly by latitude and longitude

## Slide 5: The Need for Change

## Slide 6: UN-GGIM (2015-2018)
The UN-GGIM Committee of Experts
  Endorsed the global geodetic roadmap as a “principle-based briefing document for national Governments”
  Welcomed the development of an implementation plan to link the road map recommendations to national policy developments
  Elevated the GGRF working group (WG) to a Sub-Committee on Geodesy (SCoG) to strengthen the GGRF
  Requested the development of a position paper to define the appropriate governance arrangements for the GGRF

## Slide 7: GGRF Roadmap
Global Geodetic Reference Frame
  International Terrestrial Reference Frame (ITRF)
  International Height Reference Frame (IHRF)

## Slide 8: NGS Strategic Plan
Blueprint, Part 1:
Geometric Coordinates
  NOAA Tech Rep NOS NGS 62
Blueprint, Part 2:
Geopotential Coordinates
  NOAA Tech Rep NOS NGS 64
Blueprint, Part 3:
Using the modernized NSRS
  forthcoming

## Slide 9: CORS

## Slide 10: Foundation CORS (FCORS)
Collocated
+ Densification
+ Plate Rotation
+ Additional

## Slide 11: Other CORS in the Americas
SIRGAS-CON
Canadian Active Control (CAC’s)
http://www.sirgas.org/en/sirgas-con-network/

## Slide 12: The Four TRF’s
Densified ITRF model
Control stations
  FCORS/IGS sites <=> ITRF
  Subset chosen for EPP
Four Frames after EPP
  CATRF (w/SIRGAS)
  MATRF (~ w/GGIM-AP/C.S.)
  PATRF (w/GGIM-AP)
  NATRF (IAG 1.3c/SNARF 2.0)
Intra-Frame Velocity Models

## Slide 13: NATRF
Each frame will get 3 parameters
  Euler Pole Latitude
  Euler Pole Longitude
  Rotation rate (rad/yr)
Used to compute time-dependent TRF2022 coordinates from time-dependent ITRF coordinates
To calculate a Stable North America Reference Frame, you need “stable” points

## Slide 14: CATRF (DEMETS 2007)

## Slide 15: PATRF

## Slide 16: MATRF

## Slide 17: NAPGD2022

## Slide 19: IFVM (Deformation) Modeling
Gridding CORS
CORS+Geophysical Modeling (Canadian)
CORS+InSAR

## Slide 20: CORS Horizontal Velocities-REPRO2

## Slide 21: CORS Vertical Velocities-REPRO2

## Slide 22: Canadian Vertical Velocity Model
ICE6G GIA model is fit to CAC
Fills in areas between CACs for vertical motion

## Slide 24: Questions?